## Slide 1: WF on remaining details of NB-PRACH
Huawei, HiSilicon, [Ericsson], …
R1-16xxxx
3GPP TSG RAN WG1 Meeting #84bis
Busan, Korea, 11-15 April, 2016
Agenda item 7.2.1.2.4

## Slide 2: Background on timing advance
Agreements:
  Timing relationships for random access
    For Msg3,
      The start of Msg3 transmission is the first opportunity that is >=12ms later than the end of the corresponding RAR transmission.
Since the timing advance command is conveyed in RAR, the appropriate requirement for the adjustment of the uplink transmission timing is the time for the uplink transmission immediately following RAR, i.e. Msg3.

## Slide 3: Background on timing relationships
Agreements:
Timing relationships for random access
  For NB-PRACH transmission following a PDCCH order, the start of NB-PRACH transmission is the first opportunity that is >=8ms later than the end of its associated PDCCH order.
  For Msg3,
    The start of Msg3 transmission is the first opportunity that is >=12ms later than the end of the corresponding RAR transmission.
  In case a RAR is received with no response to the corresponding NB-PRACH, the start of any new NB-PRACH transmission is the first opportunity that is >=12ms later than the end of the RAR.
  In case no RAR is received at the end of the RAR window, the start of any new NB-PRACH transmission is the first opportunity that is >=12ms later than the end of the RAR window.

## Slide 4: Observations on timing relationships
The yellow highlighted text in previous slide was added during the online discussion in Ad-hoc#2 to address a comment that it was not clear when the NB-PRACH will be transmitted by e.g. saying “>= 12ms”. The comment was valid for NB-PRACH, but not for Msg3 for which the scheduling delay should be signaled in RAR. Coupling of the time for Msg3 transmission and the end of RAR will greatly restrict the scheduling flexibility in the eNB, and can impose abandoning some of the RARs by the eNB in case of high NB-PRACH load.

## Slide 5: Background on subcarrier locations
RAN1 agreements:
The configuration of NB-PRACH resource is given by
  Periodicity (3 bits)
    {40, 80, 160, 240, 320, 640, 1280, 2560} ms
    When PRACH resource and PUSCH collide, PUSCH is postponed
  Number of repetitions (3 bits)
    {1, 2, 4, 8, 16, 32, 64, 128}
  Number of opportunities per period
    1 (no indication needed)
  Starting time of period (FFS bits)
    FFS
  Repetition uses contiguous subframes within one period
  Frequency
    Frequency location in subcarrier offset (3 bits)
      {0, 12, 24, 36, 2, 18, 34}
    Number of subcarriers (2 bits)
      {12, 24, 36, 48}
  Multi-tone Msg3 transmission is not supported for the following numbers of repetitions of NB-PRACH
    {32, 64, 128}

## Slide 6: Background on NB-PDCCH order
RAN2 agreements:
  Only Contention based RACH is supported in NB-IoT. We may revisit this if contention free RACH is found needed for positioning.
  RAN2 assumes that PDCCH order is supported for DL data arrival (and the agreement above is applicable)
RAN1 agreements:
  PDCCH order is always received in the UE-specific SS

## Slide 7: Proposals on timing advance
The adjustment of the uplink transmission timing is applied 12ms after the end of the corresponding timing advance command transmission.

## Slide 8: Proposals on timing relationships
The start of Msg3 transmission is >=12ms later than the end of the corresponding RAR transmission.

## Slide 9: Proposals on subcarrier locations
The NB-PRACH subcarrier locations are according to the following table:
 |  | “Frequency location in subcarrier offset” |  |  |  |  |  | 
 |  | 0 | 12 | 24 | 36 | 2 | 18 | 34
“Number of subcarriers” | 12 | 0 – 11 | 12 – 23 | 24 – 35 | 36 – 47 | 2 – 13 | 18 – 29 | 34 – 45
 | 24 | 0 – 23 | 12 – 35 | 24 – 47 | Invalid | 2 – 25 | 18 – 41 | Invalid
 | 36 | 0 – 35 | 12 – 47 | Invalid | Invalid | 2 – 37 | Invalid | Invalid
 | 48 | 0 – 47 | Invalid | Invalid | Invalid | Invalid | Invalid | Invalid

## Slide 10: Proposals on NB-PDCCH order
In the case of NB-PDCCH order,
  Alt1: all the bits in DCI format N1 is set to ‘0’.
  Alt2: the starting CE level is included in DCI format N1.

## Slide 11: Proposals on starting time of period
For a given NB-PRACH resource configuration, the NB-PRACH resource
  Alt1: starts at 0ms within each SFN periodicity, and the NB-PRACH opportunity occurs at “Starting time of period” within each NB-PRACH periodicity.
  Alt2: starts at “Starting time of period” within each SFN periodicity, and the NB-PRACH opportunity occurs at the beginning of each NB-PRACH periodicity.

## Slide 12: Proposals on symbol values
The symbol value for NB-PRACH is .