## Slide 1: WF on remaining details of NB-PRACH resource configuration
Huawei, HiSilicon, Nokia, Ericsson, …
R1-163598
3GPP TSG RAN WG1 Meeting #84bis
Busan, Korea, 11-15 April, 2016
Agenda item 7.2.1.2.4

## Slide 2: Proposals
For NB-PRACH configurations,
  Alt1: for each number of NB-PRACH repetitions (except 32, 64, and 128), there can be up to 2 NB-PRACH configurations.
    In the case of 2 NB-PRACH configurations, an NB-PRACH transmission using one of the configurations indicates UE support for multi-tone Msg3 transmission.
      It is up to the eNB to schedule single-tone or multi-tone transmission for Msg3.
    In the case of 1 NB-PRACH configuration, there is no indication as to whether UE supports multi-tone Msg3 transmission.
  Alt2: Preamble partitioning is used to indicate multi-tone Msg3 transmission capability
    2 bits with values {0, 1/4, 2/4, 3/4} indicating the fraction of the total number of preambles that are reserved for single-tone transmission