## Slide 1: WF on spatial filtering for TDL channel models
Huawei, HiSilicon, Qualcomm, Samsung, Ericsson
R1-163643
3GPP TSG RAN WG1 Meeting #84bis
Busan, Korea, 11th - 15th April 2016
Agenda Item: 8.2.4

## Slide 2: Background
It was agreed in Ljubljana to include the CDL and TDL models for link level simulation.
  For modeling effect of beamforming in a simplified way, an antenna pattern of brick wall (a rectangular mask) is introduced.
    This will give a TDL model from a CDL model
    Power should be normalized after the masking
    Angle scaling FFS
    Details FFS
TDL models are required for multiple purposes:
  Evaluation of link curves (e.g. BER curves)
  Evaluation of directional algorithms (e.g. beam search/tracking)
For link curves, a few exemplary TDLs are required; these TDLs are a function of beamwidth but not on the pointing angle
For directional algorithms, the TDLs are a function of beamwidth and pointing angle of the beam

## Slide 3: Basic idea
CDL Model
Delay Scaling
Angular scaling
Antenna Pattern
TDL Model

## Slide 4: Proposal for Spatial Filtering
Alternative 1: Use rectangular mask to filter the paths (BW = beamwidth).
Alternative 2: Calculate TDL based on non-rectangular filter.
    The simplified antenna pattern [ITU-R M.2135] can be used

## Slide 5: Comparison
Alternative 1
Alternative 2
Either alternative 1 or alternative 2 can be applied on a CDL to derive a TDL for evaluating directional algorithms
f
f
Paths arriving outside the beamwidth fully blocked
f
f
f
Paths arriving outside the beamwidth attenuated

## Slide 6: Proposal for Filtering
To generate TDL for link curves, we propose the following approach
  Step 1: A CDL is assumed (e.g. CDL-A)
  Step 2: The spatial filter shape and beamwidth is determined
  Step 3: The beam is pointed towards the dominant path
    correspond to the dominant path direction
  Step 4:
      A scaling parameter α is introduced.
      The TR should capture a small set of example a values based on the range of angular spreads in the channel model scenarios
  Step 5: TDL is generated by spatial filtering of the CDL by the scaled filter shape (the filter shape is stretched by α)
  Step 6: The filtered TDL is used for link level simulations
To generate TDL with arbitrary pointing direction filtered TDL power is generated by