## Slide 1: WF on Channel Coding Evaluation for 5G New Radio
3GPP TSG RAN WG1 #84bis meeting
Busan, Korea, 11th – 15th April 2016
Agenda item 8.1.6.1
Nokia, Alcatel-Lucent Shanghai Bell, Samsung, Huawei, Sony, ZTE, Intel, Qualcomm, InterDigital, NTTdocomo
R1-163757

## Slide 2: Coding Candidates
Identified channel coding schemes for each usage scenario
Common simulation assumptions are required to evaluate theoretical performance of proposed coding schemes
Selection of the coding scheme should also consider various other aspects
eMBB | mMTC | URLLC
 | Convolutional codes | Convolutional codes
LDPC | LDPC | LDPC
Polar | Polar | Polar
Turbo | Turbo | Turbo
Proposal

## Slide 3: Initial Simulation Assumptions
Simulation assumptions are separately provided for each usage scenario.
Focus mainly on the BLER performance of candidate coding schemes.
Evaluate performance of coding schemes with similar code rates and block sizes.
Exact code constructions should be provided.
  Example : Parity check matrices, polar code construction, ..
Encoding/decoding complexity of the adopted algorithms should be described.
Proposal

## Slide 4: Simulation Assumptions : eMBB
Evaluate the block error rate (BLER) performance versus SNR
  * Fading channels will be simulated in the next stage
  ** Other variants of agreed algorithms can be used for encoding and decoding (Complexity details should be illustrated)
  *** Almost similar info and encoded block lengths should be used for the evaluation. Total coded bits = info. Block length/code rate
General guidelines
  Existing code constructions can be used for evaluation
  Whenever feasible, performance comparison should adopt coding constructions with matching computational complexities
Channel* | AWGN |  |  | 
Modulation | QPSK, 64 QAM |  |  | 
Coding Scheme | Turbo | LDPC | Polar | 
Code rate | 1/5, 1/3, 2/5, 1/2, 2/3, 3/4, 5/6, 8/9 |  |  | 
Decoding algorithm** | Max-log-MAP | min-sum |  | List-X
Info. block length*** (bits w/o CRC) | 100, 400, 1000, 2000, 4000, 6000, 8000 Optional(12K, 16K, 32K, 64K) |  |  | 
Proposal

## Slide 5: Simulation Assumptions : URLLC and mMTC
Channel* | AWGN |  |  | 
Modulation | QPSK, 16 QAM |  |  | 
Coding Scheme | Convolutional codes | LDPC | Polar | Turbo
Code rate | 1/12, 1/6, 1/3 |  |  | 
Decoding algorithm** | List-X Viterbi | min-sum | List-Y | Max-log-MAP
Info. block length*** (bits w/o CRC) | 20, 40, 200, 600, 1000 |  |  | 
Evaluate BLER performance versus SNR
General guidelines
  Similar to eMBB scenario
  BLER simulations down to 10-4 is recommended (to observe the error floor) for URLLC and mMTC.
Proposal
  * Fading channels will be simulated in the next stage
  ** Other variants of agreed algorithms can be used for encoding and decoding (Complexity details should be illustrated)
  *** Almost similar encoded block lengths should be used for the evaluation. Total coded bits = info. Block length/code rate