## Slide 1: Way forward on synchronization source priority
NTT DOCOMO, Oppo, LGE
R1-163882
3GPP TSG-RAN WG1 #84b
Busan, Korea, 11th – 15th April 2016
Agenda item 7.3.2.4

## Slide 2: Proposal
Whether eNB timing or GNSS timing is prioritized can be per carrier configured by the cell on which an UE camps
  The carrier that UE camps on can be different carrier other than the carrier that the priority is configured
If the UE is configured with PC5 V2V sync. prioritization in the carrier UE performing PC5 V2V transmission ,
  If eNB timing is prioritized, UE selects eNB as the sync. source
  Else if GNSS timing is prioritized, UE selects synchronization source with priority order: GNSS > SLSS from UE with direct GNSS > FFS the priority order of other sync. source
Else
  UE selects synchronization source with the priority order specified as out of coverage case
    FFS: Priority order for out of coverage case