## Slide 1: Way forward on assumptions for waveform evaluation
Huawei, HiSilicon, InterDigital, [NTT DOCOMO], [Nokia], [Intel], [MediaTek], [Samsung], [LGE], [Ericsson], [QualComm], [Sony], [Cohere]
3GPP TSG RAN WG1 Meeting #84bis R1-163889
Busan, Korea, 11th – 15th April 2016
Agenda Item: 8.1.3

## Slide 2: Background
NR should have,
forward compatibility
multiple numerologies for many reasons, e.g. wide spectrum ranges, large bandwidth, diverse deployments and services, etc..
Waveform design is a fundamental component that needs to address the above issues, and appropriate evaluation should be defined
Evaluation method (Agreed)
Evaluation cases (Agreed)
Evaluation metrics
Evaluation parameters

## Slide 3: Proposal (Evaluation metrics)
User spectrum efficiency as performance metric
  Take into account guard band and time domain overhead. The values and their calculation method of guard band and time domain overhead should be reported.
  BLER vs SNR should be reported for calibration
  OOBE level is reported (Similar to ACLR but applied to adjacent sub-band/UE instead of carrier)
EVM (FFS: clear definition)
PAPR/Cubic metric
UE Complexity (FFS: how to quantify)
The following is also reported
  Receiver waveform design
  Rx processing delay (FFS: definition)
Power spectral density
The calculation of user spectrum efficiency is defined at the next pages

## Slide 4: Proposal (Evaluation metrics)
User spectrum efficiency is given by
 =BWcarrier is the whole bandwidth including system guard band (see above figure).
Case 1b, 2, 3, 4:
 is the data bandwidth plus guard tone of the target UE plus guard tone. (see above figure)
Case 1a:
where  denotes the number of correctly received bits by target user, T is the transmission time of the target user.  is defined as follows

## Slide 5: Proposal (Evaluation metrics)
Observation: Guard bands may not be multiples of PRB width, issue of how to implement channel coding without change of code rate or rate matcher.
Proposal:
Evaluate by which value signal transmission bandwidth could be increased without violating the spectral mask
  Can be evaluated by inspection of PSD, i.e. without extra simulation effort
Consider the possible increase number of used SC by the following equation
Issue of different filter bandwidth compared to the case of really using more SC should be negligible

## Slide 6: Proposal (Evaluation parameter for DL)
Assumptions | Value
Carrier frequency | 4GHz
Duplex | FDD/TDD
System Bandwidth | 10 MHz
TTI length | 1 ms as baseline, other TTI length is FFS ( short TTI should be considered)
Subcarrier spacing | Single numerology case: 15KHz as baseline, Mixed numerology case: 15KHz, and the other subcarrier spacing FFS
Guard time interval | 4.7us (interval of LTE normal CP) as baseline, other interval is FFS
FFT size | 1024 for 15KHz subcarrier spacing
Data transmission bandwidth | Single numerology case: Mixed numerology case: At least two candidate BWs for target UE. At least two candidate BWs for interfering subband At least two numerologies. The values are FFS
Guard tone number | [0~10 ]subcarriers for the mixed numerology case
Number of Tx antenna ports | 1T1R, 4T4R
MIMO mode | TM3
Rank per UE | Fixed rank4 for 4T4R
MCS | Fixed. 16QAM: 1/2, 2/3; 64QAM: 1/2, 3/4;256 QAM: 1/2, 3/4
Control Overhead | No RS, PDCCH / EPDCCH / PSS / SSS / PBCH
Channel estimation | Ideal
Channel Model | ETU for 3km/h mobility (mandatory) EVA for 120km/h mobility (optional)
Table 1 Parameters for case 1 and case 2

## Slide 7: Proposal (Evaluation parameter for UL)
Table 2 Parameters for case 3 and case 4
Assumptions | Value
Carrier frequency | 4GHz
Duplex | FDD /TDD
TTI length | 1 ms as baseline, other TTI length is FFS ( short TTI should be considered)
Subcarrier spacing | Single numerology case: 15KHz as baseline, Mixed numerology case: 15KHz, and the other subcarrier spacing is FFS
Guard time interval | 4.7us as baseline, other interval is FFS
FFT size | 1024 for 15KHz subcarrier spacing
Bandwidth per user (including target user and interfering user) | 720 KHz (48 Subcarriers allocated per user)
Number of uplink users | 3 (1 target user and 2 interfering users)
Power offset of the interfering user | 0 dB, 10 dB , 20 dBs
Number of transmission antenna ports | 1T1R
MCS | Fixed. 16QAM: 1/2, 2/3; 64QAM: 1/2, 3/4
Control Overhead | No
Time offset of interfering user | Case 3 only: 0, 128, 512 samples (for 15 KHz subcarrier spacing)
Channel estimation | Ideal
Guard tone number | [0 ~10] Subcarriers
Channel Model | ETU for 3km/h mobility (mandatory) EVA for 120km/h mobility (optional)

## Slide 8: Other Evaluation detailed assumption
Proposal: Consider the RF nonlinearity in the evaluation cases of R1-163558. And
RAN1 can consider the following models for PA modeling, i.e. Rapp model [1] (AM/AM, AM/PM) and/or Clipping model with different thresholds
  Companies should provide the model parameters (operating point, back-off value etc.) and justification (i.e. EVM, OOBE/PSD)
2. Huawei to draft a LS to RAN4 to ask on the applicability/fidelity of the models above for both UE and BS, different carrier frequency and signal bandwidth, and recommend parameters (operating point, back-off value etc.) to be used in the models or recommend realistic other PA models.
[1]“Comparison of Power Amplifier Non-linearity Impact on 60 GHz Single Carrier and OFDM Systems”, Maltsev at al., IEEE CCNC 2010.