## Slide 1: Clarifications on O-I implementation
Nokia, AT&T, Ericsson, ETRI, Huawei, HiSilicon, Intel, KT Corporation, NTT DOCOMO, Qualcomm, Samsung
3GPP TSG RAN WG1 Meeting #85 R1-164617
Nanjing, China 23rd - 27th May 2016

## Slide 2: Some uncertainties in current O-I modelling
O-I deviation: Is it an add-on term or replacement of SF? Is it UE specific, site specific or link specific?
Random generation of d_in? UE, site or link specifics?
Note: Link specific means one random variable is generated for each BS-UE link. UE specific means one random variable is generated for the UE (common for all links to this UE). Site specific means one random variable is generated for all the links from one site to one UE.
PL = PLb + PLtw + PLin + N(0, σP)

## Slide 3: Comparing the Coupling loss (Using UMi-30Ghz as example)
Link specific O-I implementation introduces some selective gain on serving cell’s coupling loss (up to 6dB at cell edge part)

## Slide 4: Consideration on d_in implementation
Distances to external walls is UE-specific
Propagation path from/to different BS sites may go through different walls
  d2D-in is likely correlated for different sites
  Sites in similar direction => same d2D-in
  Sites in opposite directions => different d2D-in
For rectangle building 4 completely independent d_in can be found.
UE
BS1
BS3
BS2
Conclusion: Neither link specific or UE specific implementation is completely accurate. Comparably, UE specific is more close to reality.

## Slide 5: Proposal
Clarify the implementation of O-I in TR38.900 as following:
  The selection of high loss or low loss O-I model is UE specific
  O-I deviation is an add-on term to SF.
    Change the standard deviation to 4.4 and 6.5 for low loss and high loss penetration model separately (see below table from R1-163256)
    O-I deviation is UE specific random variable.
  d_in is an UE specific random variable