## Slide 1: WF on Supported NR Operations
Samsung, Nokia, ALU Shanghai Bell,
R1-165559
3GPP TSG RAN WG1 #85
Nanjing, China, 23rd – 27th May 2016
Agenda item 7.1.6

## Slide 2: Proposals
RAN1 to strive for both beam-centric operation and non-beam-centric operation in a single unified framework
  Beam-centric operation
    In beam-centric operation, multiple beams are used for covering a DL/UL coverage area of a TRP/a UE.
    One example of beam-centric operation is beam sweeping:
      When beam sweeping is applied for a signal (or a channel), the signal (the channel) is transmitted on multiple beams, which are on multiple time instances in a constant time duration.
  Non-beam-centric operation
    In non-beam-centric operation, a single beam can be used for covering a DL/UL coverage area of a TRP/a UE, similarly as for LTE cell-specific channels/RS.

## Slide 3: Proposals
For beam-centric operation, study the application of beam sweeping at least for:
  Initial-access signals (synchronization signals and random access channels)
  System-information delivery (broadcast channels)
  RRM measurement
  CSI measurement