## Slide 1: WF on NR UL MIMO
Intel, NTT DoCoMo
R1-165586
3GPP TSG RAN1 #85
Nanjing, China, May 23 - 27, 2016
Agenda Item: 7.1.6

## Slide 2: Background
In R1-163884, R1-163885 and email discussion [84b-13], number of antenna elements at TRP/UE is agreed:
  @700MHz: up to 64 @TRP and up to 4 @UE
  @4GHz: up to 256 @TRP and up to 8 @UE
  @30GHz: up to 256 @TRP and up to 32 @UE
  @70GHz: up to 1024 @TRP and up to 32 @UE
With larger number of antenna elements @TRP at all NR bands and new UE hybrid antennas @UE, this WF tries to summarize companies’ views with regard to NR UL MIMO design
In order to fully reap the gain of large number of antennas in NR system, UL MIMO needs to be enhanced compared to LTE UL MIMO

## Slide 3: NR UL MIMO technologies
The following techniques are studied for NR UL MIMO
  Uplink transmission/reception schemes
    Spatial multiplexing
      Non reciprocity based UL MIMO (e.g. PMI based)
      Reciprocity based UL MIMO
      @>6GHz,
        UL analog beamforming management
        Multi point spatial multiplexing
    Spatial diversity
      open loop and semi-open loop UL MIMO
      Uplink antenna / panel switching
      Multi point reception
      @>6GHz
        Multi panel spatial diversity
  SRS/DMRS design for UL MIMO
  UL power/timing control
  UL control channel
  Other techniques are not precluded