## Slide 1: Way forward on remaining issues on multiple access evaluation assumptions
Huawei, HiSilicon, […]
3GPP TSG RAN WG1 Meeting #85 R1-165847
Nanjing, China, 23rd – 27th May 2016
Agenda Item: 7.1.2

## Slide 2: Background
In RAN1#84bis, evaluation method, metrics, scenarios, and preliminary LLS evaluation assumptions were agreed.
Email discussions [84b-11] LLS assumptions for multiple access for NR and [84b-12] SLS assumptions for multiple access for NR were conducted, and further agreements on some LLS parameters were achieved.
Remaining issues on LLS and SLS parameters needs to be addressed in RAN1#85:
  Further discussion on key parameters for LLS, e.g., target spectral efficiency per user and total allocated bandwidth.
  SLS detailed parameters for identified scenarios and other SLS related issues.

## Slide 3: Proposal (LLS remaining issues)
  PHY abstraction from LLS should be provided for calibration purpose
  Further LLS evaluation with more aligned parameters are needed for calibration of PHY abstraction
    The remaining parameters such as total allocated bandwidth and target spectral efficiency should be chosen to reflect the typical values in SLS
  For channel estimation in LLS, ideal and realistic results need to be provided.

## Slide 4: Proposal (SLS parameters)
SLS parameters for eMBB scenario – Rural
Attributes | Values or assumptions
Layout | Single layer - Macro layer: Hex. Grid
Inter-BS distance | 1732m
Carrier frequency | 700 MHz
Simulation bandwidth | 20MHz
Channel model | RMa
Tx power | BS: 49dBm / 20MHz UE: Max 23dBm
BS antenna configuration | 2/4/8 Tx/Rx ports as start point,
BS antenna pattern | Follow the modeling of TR36.873
BS antenna tilt | Companies report tilt
BS antenna height | 35 m
BS antenna element gain + connector loss | 8 dBi
BS receiver noise figure | 5 dB
UE antenna elements | 1 Tx and 2 Rx as starting point
UE antenna height | 1.5m
UE antenna gain | Follow the modeling of TR36.873
UE receiver noise figure | 9 dB
Traffic model | For TRP spectrum efficiency: full buffer For user experienced data rate: non-full buffer; FTP model 3
Traffic load (Resource utilization) | 25%, 50%, 80% (other value is not precluded)， Packet size: 0.5MB; 0.1MB; other values not precluded
UE distribution | Uniform distribution, 10, 20 users per TRP or more for full buffer traffic 50% outdoor vehicles (120km/h) and 50% indoor (3km/h)
UE receiver | Advanced receiver can be considered
BS receiver | Advanced receiver can be considered
Feedback | Realistic
Channel estimation | Realistic*
*NOTE: ideal channel estimation results for calibration

## Slide 5: Proposal (SLS parameters)
SLS parameters for eMBB scenario – Dense urban
Attributes | Values or assumptions
Layout | Single layer - Macro layer: Hex. Grid
Inter-BS distance | 200m
Carrier frequency | Around 4 GHz
Simulation bandwidth | 20MHz
Channel model | 3D UMa (Macro layer)
Tx power | BS: Macro layer: 44 dBm / 20MHz UE: Max 23dBm
BS antenna configuration | 2/4/8 Tx /Rx ports as start point, other number of antenna ports could be evaluated
BS antenna pattern | Follow the modeling of TR36.873
BS antenna height | 25m for macro cells
BS antenna tilt | Companies report tilt
BS antenna element gain + connector loss | 8 dBi
BS receiver noise figure | 5 dB
UE antenna elements | 1 Tx and 2 Rx as starting point
UE antenna height | Follow TR36.873
UE antenna gain | Follow the modeling of TR36.873
UE receiver noise figure | 9 dB
Traffic model | For TRP spectrum efficiency: full buffer For user experienced data rate: non-full buffer; FTP model 3
Traffic load (Resource utilization) | 25%, 50%, 80% (other value is not precluded)， Packet size: 0.5MB; 0.1MB; other values not precluded
UE distribution | Uniform distribution, 10, 20 users per TRP or more for full buffer traffic 80% indoor (3km/h), 20% outdoor (30km/h)
UE receiver | Advanced receiver can be considered
BS receiver | Advanced receiver can be considered
Feedback | Realistic
Channel estimation | Realistic*
*NOTE: ideal channel estimation results for calibration

## Slide 6: Proposal (LLS parameters)
Parameters | Values or assumptions
Suggested target spectral efficiency Definition: required transmission bits per user / total number of resource elements shared for data transmission | Companies need to report the values of target spectral efficiency. Following values could be start point: 0.125bps/Hz, 0.25bps/Hz, 0.375bps/Hz, 0.5bps/Hz Other values are not precluded.
Table 1: Additional parameters for UL
  Additional parameters

## Slide 7: Proposal (Baseline)
  The comparison baseline could be
  Baseline 1: LTE RACH and grant-based orthogonal MA
  Baseline 2: LTE OFDMA with contention based transmission