## Slide 1
3GPP TSG-RAN1 Meeting #86 R1-167957
Gothenburg, Sweden, 22nd – 26th Aug 2016
WF on evaluation assumptions for initial access in NR
Intel Corporation, […]
Agenda item: 8.1.6

## Slide 2: Link-level evaluation assumptions
 | Below 6GHz | Above 6GHz
Carrier Frequency | 4 GHz | 30, 70 GHz
Channel Model | CDL, AWGN | 
Subcarrier Spacing | 15, 30, 60, 120 or 240 kHz (to be clarified by each company) | 
SNR range | > -6dB | > -18dB
Search window | The time window to search (correlate) NR-PSS. It depends on the periodicity of NR-SS transmission. The value needs to be provided by each company. | 
Antenna Configuration at the TRP | (1,1,2) with omni-directional antenna element | (4,8,2), with directional antenna element (HPBW=650, directivity 8dB)
Antenna Configuration at the UE | (1,1,2) with omni-directional antenna element | (2,4,2), with directional antenna element (HPBW=900, directivity 5dB)
Antenna port virtualization | Clarified by each company in simulation assumptions | 
Frequency Offset | Initial acquisition TRP: uniform distribution +/- 0.05 ppm UE: uniform distribution +/- 10 ppm (optional: 5 ppm, 20ppm) Non-initial acquisition TRP: uniform distribution +/- 0.05 ppm UE: uniform distribution +/- 0.1 ppm | 
Number of interfering TRPs | 1. 0 TRP 2. 2 interfering TRPs (1st SIR = 0 dB, 2nd SIR = -3dB) – timing arrival differences from TRPs are provided by each company | 1. 0 TRP

## Slide 3: System-level evaluation assumptions
 | Below 6GHz | Above 6GHz
Scenario | Urban Macro, ISD = 500m | 
Carrier Frequency | 4 GHz | 30, 70 GHz
Channel Model | TS 36.873 | TS 38.900
UE dropping | According to TS 36.873 | 
Subcarrier Spacing | 15, 30, 60, 120 or 240 kHz (to be clarified by each company) | 
Network Synchronization | TRPs are synchronized, propagation delay difference between TRPs is modelled. | 
Search window | The time window to search (correlate) NR-PSS. It depends on the periodicity of NR-SS transmission. The value needs to be provided by each company. | 
Antenna Configuration at the TRP | (1,1,2) with directional antenna element (HPBW=650, directivity 8dB) | (4,8,2), with directional antenna element (HPBW=650, directivity 8dB)
Antenna Configuration at the UE | (1,1,2) with omni-directional antenna element | (2,4,2), with directional antenna element (HPBW=900, directivity 5dB)
Frequency Offset | Initial acquisition TRP: uniform distribution +/- 0.05 ppm UE: uniform distribution +/- 10 ppm (optional: 5 ppm, 20 ppm) Non-initial acquisition TRP: uniform distribution +/- 0.05 ppm UE: uniform distribution +/- 0.1 ppm | 
PHY Abstraction | No PHY Abstraction. All the links shall be explicitly implemented in the system level platform. | 

## Slide 4: Performance metrics
Signal detection rate
Misdetection probability
Distribution of acquisition time (a.k.a. cell search time)
Residual timing and frequency errors after synchronization
Other metrics are not precluded