## Slide 1: WF on UL DMRS
Nokia, Alcatel-Lucent Shanghai Bell, Huawei, HiSilicon
3GPP TSG RAN WG1 Meeting #86
Gothenburg, Sweden, 22 – 26 August 2016
Agenda item: 7.2.4.1.3
R1-167972

## Slide 2: Proposal: UL DMRS Enhancement
Support orthogonal DMRS (more than 2) for MU-MIMO with partial overlapping BW allocation by
  IFDMA with both RPF 2 and RPF 4

## Slide 3: Proposal: IFDMA Sequence Design
Following new IFDMA sequence lengths shall be supported and designed:
  For new lengths larger than 36, IFDMA DMRS sequence is generated by legacy mechanism with the extension of a Zadoff-Chu sequence
    FFS: whether root sequence index shall be modified
  For RPF=2, at least DMRS lengths of 6, 18, 30 are supported
    FFS: Exact DMRS sequences of these lengths TBD until next meeting
  For RPF=4, at least DMRS lengths of 3, 9, 6, 18, 30 are supported
    FFS: Exact DMRS sequences of these lengths TBD until next meeting
Seq L | 1PRB | 2 | 3 | 4 | 5 | 6 | 8 | 9 | 10
RPF 2 | 6 | 12 | 18 | 24 | 30 | 36 | 48 | 54 | 60
RPF 4 | 3 | 6 | 9 | 12 | 15 | 18 | 24 | 27 | 30

## Slide 4: Proposal: CS and Power Boosting
FFS: whether and how CS of DMRS generation shall be modified to improve backward compatibility for the pairing with legacy UE.
Additional power boosting shall be supported and applied to IFDMA DMRS depending on the value of RPF
  FFS: x dB for RPF 2 and y dB for RPF 4