## Slide 1: WF on design principle of search space for NB-IoT SC-PTM
Huawei, HiSilicon, ITL, […]
R1-167988
3GPP TSG RAN WG1 Meeting #86
Gothenburg, Sweden, August 22-27, 2016
Agenda item 7.2.11.2

## Slide 2: Background
In NB-IoT’s Rel-14 WID, multi-cast downlink transmission is expected to be supported based on Rel-13 SC-PTM
  Introduction of necessary enhancements to support narrowband operation, e.g. support of NPDCCH, and coverage enhancement, e.g. repetitions
Search space should be defined for NB-IoT multicast considering the capability of NB-IoT UEs, e.g. no possibility to simultaneously monitor two different search spaces.

## Slide 3: Proposal
Monitoring of search spaces, DCI formats, RNTIs for SC-PTM:
  No increase in the number of blind decoding attempts in a subframe compared to Rel-13 NB-IoT.
  No reduction in the amount of time to complete the blind decodes, i.e. minimum gap between search spaces for the same UE is 4ms
SC-MCCH change notification procedure will be modified for NB-IoT
  DCI addressed to SC-N-RNTI will not be used
Introduce new search space type for SC-MTCH
  Individual search space configurations are supported per SC-MTCH.