## Slide 1: WF on Aperiodic CSI-RS for Rel.14
Samsung, Nokia, Alcatel-Lucent Shanghai Bell, KT Corporation, Ericsson, LG Electronics, Interdigital, Qualcomm, AT&T, CHTTL, Xinwei, Straightpath, ITL
3GPP TSG RAN WG1 Meeting #86
Gothenburg, Sweden 22nd - 26th August 2016
Agenda item: 7.2.4.1.2
R1-168046

## Slide 2: Background
From RAN1#85:
Agreement: Scheme 1: Aperiodic NZP CSI-RS resource is supported in Rel-14 for Class B eMIMO-Type, where Only PUSCH based A-CSI reporting is supported. A new aperiodic CSI-RS resource allocation/configuration is defined Without Subframe_config Aperiodic CSI-RS transmission instance is indicated by UL-related DCI transmitted on a control channel with a CSI request field: Aperiodic CSI-RS transmission is in the same DL subframe as the associated UL-related DCI FFS whether or not the UE may not assume more than one aperiodic NZP CSI-RS resource. If more than one resource is allowed, FFS the signaling details FFS the number of bits for the CSI request field The control channel can be PDCCH or EPDCCH. FFS whether or not the case of EPDCCH can be precluded or with some restrictions/relaxations FFS whether or not periodic CSI-RS can be additionally configured Scheme 2: For Class B eMIMO-Type, the following CSI-RS resource configuration mechanism is supported A UE receives an activation/release trigger containing a choice from multiple higher-layer-configured NZP CSI-RS resources for a given CSI process Each NZP CSI-RS resource can be either periodic or, aperiodic CSI-RS resource (if scheme 1 is supported) Details of the activation/release trigger (including the set of NZP CSI-RS resource configuration parameters) are FFS For an activation trigger received in subframe n, the transmission of the associated NZP CSI-RS resource will start no earlier than subframe n+X where X>0 For a release trigger received in subframe n, the transmission of the associated NZP CSI-RS resource will stop after subframe n+Y where Y>0 FFS the impact of multi-shot configuration, if supported FFS whether or not there are any significant issues regarding the potential misalignment about activation and/or release between eNB and UE, and if so, how to address them FFS whether or not to further enhance rate matching for PDSCH, particularly whether or not aperiodic NZP CSI-RS will not have impact on PDSCH RE mapping FFS the QCL details Down-selection between scheme 1 and scheme 2 (if any) to be discussed in RAN1#86

## Slide 3: Proposal – aperiodic CSI-RS (1/2)
Two-step NZP CSI-RS resource configuration:
  Step 1. RRC configuration with a newly defined Aperiodic CSI-RS-Resource-Config IE
    Without Subframe_config
    Configure a UE with K = {1, 2, .., 8} CSI-RS resources
  Step 2. Semi-persistent using activation/release mechanism
    Activate N out of K CSI-RS resources per CSI process
    Up to N NZP CSI-RS resources may be simultaneously active in a UE
      Once activated, a CSI resource remains activated until released
    Choose at least one of the following alternatives for activation/release mechanism (TBD in RAN1#86bis)
      Alt1. Using UL grant(s)
        FFS: Support for cross-carrier activation/release
      Alt2. Using MAC CE
      Other alternatives are not precluded
      FFS the values of X and Y, how to select N
(cont’d)

## Slide 4: Proposal – aperiodic CSI-RS (2/2)
(cont’d)
One out of N CSI-RS resources is selected via the UL-related DCI
  A UL grant carries a CSI request and indicates transmission of one CSI-RS resource if N>1 aperiodic CSI-RS resources are activated for a CSI process for which the CSI is requested
    A CSI request is for one CSI-RS resource per CSI process
    Choose one out of the following alternatives for indicating transmission of 1 out N CSI-RS resources (TBD in RAN1#86bis)
      Alt1. use code points from an existing DCI field to select 1 out N CSI-RS resources
      Alt2. Introduce additional bit(s) in DCI
      Note: The number DCI fields and number of code points for the combinations of CSI process, CC and CSI-RS resource indication are FFS
Only PUSCH based A-CSI reporting is supported
    Aperiodic CSI-RS transmission is in the same DL subframe as the associated UL-related DCI
Whether and, if needed, how to support CSI processing relaxation for aperiodic CSI-RS are TBD

## Slide 5: Proposal – “Multi-shot” CSI-RS
Two-step NZP CSI-RS resource configuration:
  Step 1. RRC configuration with a Rel-13 periodic CSI-RS-Resource-Config IE
    Configure a UE with K = {1, 2, .., 8} CSI-RS resources
  Step 2. Semi-persistent using activation/release mechanism
    Activate N out of K CSI-RS resources per CSI process
    Up to N NZP CSI-RS resources may be simultaneously active in a UE
      Once activated, a CSI resource remains activated until released
    Choose at least one of the following alternatives for activation/release mechanism (TBD in RAN1#86bis)
      Alt1. Using UL grant(s)
        FFS: Support for cross-carrier activation/release
      Alt2. Using MAC CE
      Other alternatives are not precluded
      FFS the values of X and Y, how to select N
CSI reporting
  N=1: CQI/PMI/RI is reported
  N>1: CRI (=0,1, …, N – 1) is reported along with CQI/PMI/RI associated with the reported CRI value

## Slide 6: Proposal – Overhead reduction for Class B
Support CSI-RS frequency-domain density reduction for Class B
  Configurable between “legacy density (1 RE/RB/port)” and “density reduction”