## Slide 1: WF on resource pool signaling
LG Electronics, Huawei, ITRI
3GPP TSG RAN WG1 Meeting #86 R1-168060
22nd – 26th August, 2016 Gothenburg, Sweden
Agenda item: 7.2.2.3

## Slide 2: Proposals
Support two methods for frequency resource indication for resource pool
  Method 1: Reuse Rel-12 signaling method for SA and data pool
    Used for SA/data TDMed or FDMed in non-adjacent PRBs
  Method 2: A new method to additionally support the interleaved SA and data pool
    Used for SA/data FDMed in adjacent PRBs
    The inter-SA gap is signaled and SA resources are included in the indicated sub-bands and separated by the inter-SA gap.
Single bitmap is used the set SL subframes common to SA and data pools.
  Bitmap length is up to RAN2

## Slide 3
Examples of two sub-bands indicated case for each resource pool
Method#1 Method#2
SA pool
SA pool
Data pool
Data pool
time
freq.
Inter-SA gap