## Slide 1: WF on number of HARQ processes to support for NR
Qualcomm
3GPP TSG RAN WG1 #86 R1-168092
Gothenburg, Sweden, Aug 22 - 26, 2016
Agenda item: 8.1.3

## Slide 2: Observations
The support of self-contained single interlace operation is useful for the following use cases:
  Ultra reliability low latency communication
  Forward compatibility
  Low complexity high throughput support
  Dynamic TDD
  NR over unlicensed band
  …

## Slide 3: Way Forward
As one operating mode, at least the following is supported in the spec:
  1 HARQ process (only applicable for TDD):
    A UE can be configured with back-to-back single HARQ process:
      ACK in SF(N); reTx in SF >= (N+1)
  More than 1 HARQ processes:
    Option 1: 2 HARQ processes
      For FDD, A UE can be configured with:
        ACK in SF(N+1); reTx in SF >= (N+2)
      For TDD, A UE can be configured with one of the two options:
        Option 1: ACK in SF(N); reTx in SF >= (N+2)
        Option 2: ACK in SF(N+1); reTx in SF >= (N+2)
    Option 2: 3 HARQ processes
      For FDD/TDD, A UE can be configured with:
        Option a: ACK in SF(N+1); reTx in SF >= (N+3)
        Option b: ACK in SF(N+2); reTx in SF >= (N+3)
  Others # of HARQ processes: FFS