## Slide 1: WF on RACH procedure for NR
NTT DOCOMO, Ericsson, Nokia, Alcatel-Lucent Shanghai Bell, [Huawei, Qualcomm, ZTE ….]
3GPP TSG RAN WG1 Meeting #86
Göteborg, Sweden 22nd - 26th August 2016
Agenda: 8.1.6
R1-168124

## Slide 2: Proposals (General)
RACH procedure including RACH preamble (Msg. 1), random access response (Msg. 2), message 3, and message 4 is at least assumed for NR from RAN1 perspective
Simplified RACH procedure, e.g., Msg. 1 (UL) and Msg. 2 (DL), should be further studied
  Details on Msg. 1 and Msg. 2 are FFS

## Slide 3: Proposals (Beam-forming)
The design of the random access procedure should take into account the possible use of multi-beam DL and multi-beam UL as well as multi-beam DL and single-beam UL
In case that beam-forming is applied to DL broadcast channels/signals for initial access, association between DL broadcast channels/signals detected by UE for initial access and RACH resource is considered.
  FFS: Details on association in the context of multi-beam DL - multi-beam UL and multi-beam DL - single-beam UL
Multiple occasions for RACH preamble transmission in a given time interval is supported
  FFS: Details on time interval
Allow for RACH reception/RAR transmission in TRPs other than the one transmitting synchronization signals