## Slide 1: Way Forward on MUST DCI Design for Case 1&2
Qualcomm, Nokia, ABS, NEC, …
R1-168328
3GPP TSG-RAN WG1 #86
Gothenburg, Sweden, 22nd – 26th Aug 2016
Agenda item 7.2.5.2

## Slide 2: Background
The RAN1 #85 agreement is:
  At least one new DCI is to be monitored by a UE once configured into MUST operation
    FFS on details
From RAN4 study, the BD for interference existence and power ratio is not reliable

## Slide 3: Proposal
Consider the following options for providing MUST-near UE co-schedule information
  Alt 1. Single DCI by adding bits in the self DCI
    Option 1: Assumes full RA alignment
      Carries tx scheme indicator (MUST/SU-MIMO) and power ratios indices in all supported DCI formats for MUST-near UE
      FFS: Number of additional bits needed
    Option 2: Do not assume full RA alignment
      Joint encoding MUST-far UE information and MUST-near UE information in a longer MUST-near UE DCI
      FFS: Exact design
  Alt 2. Use common companion DCI to carry all MUST-far UE information
    Do not assume RA alignment
    FFS: Anything to add to MUST-near UE DCI
  Alt3. Use user-specific companion DCI to carry all MUST-far UE information within near-UE allocation
    Do not assume RA alignment
    FFS: What to add to MUST-near UE DCI