## Slide 1: WF on CP overhead
ZTE, ZTE Microelectronics,Qualcomm
3GPP TSG RAN WG1 #86
Gothenburg, Sweden August 22-26, 2016
Agenda item:8.1.3.1
Document for decision
R1-168338

## Slide 2: Observations
In [1] [2] [3], for the evaluated scenarios, scaled numerology shows better performance than ECP
  [1] R1-166360-URLLC numerology and frame structure designs, QComm
  [2] R1-164691-NR numerology design and evaluation for long delay spread channels, Qcomm
  [3] R1-164272-Performance evaluation of numerology candidates (URLLC case)
In [4] [5] [6] [7] [8], for evalauted scenarios extended CP show benifits
  [1] R1-166100, Huawei, Hisilicon
  [2] R1-166652, Sony
  [3] R1-166879, LGE
  [4] R1-167107, CMCC
  [5] R1-167108, CMCC

## Slide 3: Observations
Overhead of LTE- ECP is significant
The CP overhead is especially important for the 60 kHz SCS case
ECP requires a change of time domain structure compared to NCP
There exist different design choices for different CPs, for example
  Semi-extended 1 (Ericsson): 26 symbols / 0.5ms => 2.56 us CP, 13.33% overhead
  Semi-extended 2: 27 symbols / 0.5 ms => 1.85 us ,10% overhead
  Semi extended 3: 25 symbols / 0.5ms => 16,67 % overhead
  Keep the same number of symbols as NCP, but change DFT size

## Slide 4: Proposals
CP overhead should be studied, especially for the case of 60 kHz subcarrier spacing.
NR should support solutions with the same or better performance than LTE in all channel conditions