## Slide 1: Way forward on pedestrian UE resource selection
NTT DOCOMO, Huawei, HiSi
R1-168385
3GPP TSG RAN WG1 Meeting #86
Gothenburg, Sweden 22nd - 26th August 2016
Agenda item 7.2.3.2

## Slide 2: Background
In TR 36.885
  In section 7.1
    It needs to be further discussed in Stage 3 whether a separate pool is needed for P2X or the common pool used for V2X and I2X can be also used for P2X.
  In conclusion
    It is recommended to support following solutions identified in this TR for PC5-based V2X:
      Random resource selection for P-UEs potentially on the resource pool shared with V-UE transmissions, with additional study on sensing operation during a limited time for P-UEs

## Slide 3: Proposal
If shared Tx resource pool is used by pedestrian UEs and vehicle UEs
  Pedestrian UE can sense in a subset of subframes and skip sensing in other subframes for energy saving
    FFS details on how/when UE skip sensing
    Vehicle UE resource selection is reused as the baseline for pedestrian UE resource selection
      FFS details
  FFS whether pedestrian UE can skip sensing in all the subframes and use random resource selection