## Slide 1: WF on NR frame structure
NTT DOCOMO, INC., Panasonic
3GPP TSG RAN WG1 Meeting #86bis
Lisbon, Portugal 10th –14th October 2016
Agenda: 8.1.2
R1-1610482

## Slide 2: Proposal (1)
Define a subframe duration as 1ms with a reference numerology of 14 symbols at 15kHz SCS with NCP.
The NR frame structure supports both slot and mini-slot.
  For the slot duration y, following is supported.
    Configurations supporting slot y=7 and 14 for SCS of up to 60kHz with NCP.
    y=14 for SCS higher than 60kHz with NCP.
  For the mini-slot duration, following is supported.
    2-symbol duration for 15kHz SCS.
    FFS other SCS and/or other number of symbols.
  Following usages of a slot are enabled.
    DL-only
    UL-only
    DL part and UL part with one DL-to-UL switching point
  Within a mini-slot, there is no DL-to-UL switching point

## Slide 3: Proposal (2)
For Time alignment among different numerologies for the same CP overhead,
  Adopt Alt.1 of R1-1609048.