## Slide 1: WF on RACH Procedure for Multi-beam Operation
NTT DOCOMO, ETRI, Qualcomm, Nokia, Alcatel-Lucent Shanghai-Bell, ZTE
3GPP TSG RAN WG1 Meeting #86bis
Lisbon, Portugal 10th –14th October 2016
Agenda: 8.1.5.2
R1-1610489

## Slide 2: Background
Agreements at RAN1#86:
The design of the random access procedure should take into account the possible use of single-beam and multiple beam operations, including
  Non Rx/Tx reciprocity at BS or UE
  Full or partial Rx/Tx reciprocity at BS or UE
In case that multiple beam-forming is applied to DL broadcast channels/signals for initial access,
  RACH resource is obtained by UE from detected DL broadcast channels/signals
    FFS: Details on association
  Other mechanism w/o association is also considered
Multiple occasions for RACH preamble transmission in a given time interval are considered
  Details are FFS
  Other mechanism is not precluded
Study further RACH reception/RAR transmission in TRPs/beams other than the one transmitting synchronization signals

## Slide 3: Background
  BS can generate similar beam patterns between DL and UL in the presence of reasonable device reciprocity [1]
  Beam strength estimation of a particular beam remains valid for the time gap between DL SYNC and UL RACH sub-frames at pedestrian velocity [1]
  During random access procedure, it is desired that beam-forming in multi-beam operation is applied in earlier stage of the procedure regardless of whether Tx/Rx reciprocity at gNB and UE is available or not
[1] R1-1610150, “Effect of Calibration in Beam Gain and Beam Coherence Time”, Qualcomm Inc, 3GPP TSG RAN WG1 Meeting #86b, Lisbon, Portugal

## Slide 4: Proposals
  When Tx/Rx reciprocity is available at both gNB and UE, the following RACH procedure is considered for at least UE in idle mode
  Association between one or multiple occasions for DL broadcast channel/signal and a subset of RACH occasions is partially or fully informed by broadcast system information (e.g., PBCH)
    Signaling of “non-association” can be also included
    Detailed design for RACH preamble should be further studied
  Based on the DL Tx beam measurement and the corresponding association, UE selects the subset of RACH occasions
  At gNB, the DL Tx beam for the UE is obtained based on the detected RACH preamble and would be also applied to Message 2
    UL grant in message 2 may indicate the transmission timing of message 3.

## Slide 5: Proposals
  For the cases with and without Tx/Rx reciprocity, the common random access procedure should be strived.
  When Tx/Rx reciprocity is not available, the the following could be further considered for at least UE in idle mode
  Whether or how to report DL Tx beam to gNB, e.g.,
    RACH preamble
    Msg. 3
  Whether or how to indicate UL Tx beam to the UE, e.g.,
    RAR