## Slide 1
3GPP TSG RAN WG1 Meeting #86bis R1-1610490 Lisbon, Portugal, 10th - 14th Oct 2016
Agenda item: 8.1.4.4
WF on NR CSI-RS
Huawei, HiSilicon,……

## Slide 2: Background
Following WF has been agreed in RAN1#86:
  Study RS pattern for CSI measurement in NR both for DL and UL
    Study the density of RS
    Study the position of RS in the [subframe]
    Study the mapping of RS in one or several symbols

## Slide 3: Proposal
Support the following functionalities in NR CSI-RS design
  CSI measurement
  Beam measurement
  RRM measurement
Support NR CSI-RS pattern with at least the following properties:
  CSI-RS mapped in one or multiple consecutive symbols
  At least CSI-RS located at the earlier part of a slot
    FFS: before or after the DM RS agreed to study in RAN1#85
  FFS: CSI-RS located at other part of a slot
  Configurable density of CSI-RS in frequency domain
  FFS: CSI-RS for NR should support up to at least 32 ports

## Slide 4
Support at least following configurations of NR CSI-RS
  UE-specific configuration to support
    Wideband CSI-RS, i.e. the full bandwidth the UE is configured to operate with
    Subband CSI-RS, i.e. part of the bandwidth the UE is configured to operate with