## Slide 1: WF on UL link adaptation procedures in NR
LG Electronics, CATT
R1-1610526
3GPP TSG RAN1 #86bis
Lisbon, Portugal, Oct. 10 – 14, 2016
Agenda Item: 8.1.4.2.

## Slide 2: Proposals
Precoded/non-precoded SRS based UL link adaptation procedures should be supported in NR, with at least following different procedures:
  PUSCH scheduling (MCS/precoder/rank) is based on non-precoded SRS transmission by UE
    Configurable number of SRS ports are 2, 4, or [8].
    FFS on precoder/codebook
  PUSCH scheduling (MCS/precoder/rank) is based on precoded SRS(s) transmission by UE
    Configurable number of SRS ports are 1, 2, or [4].
    Multiple precoded SRS resources can be configured.
    FFS on precoder/codebook
  PUSCH scheduling (MCS/precoder/rank) is based on a combination of non-precoded and precoded SRS transmission by UE.