## Slide 1: WF on NB IoT SC-PTM scheduling
Ericsson …
R1-1610551
3GPP TSG RAN WG1 Meeting #86bis
Lisbon, Portugal, 10th – 14th Oct 2016
Agenda item 7.2.9.2

## Slide 2: Background
In NB-IoT’s Rel-14 WID, multi-cast downlink transmission is expected to be supported based on Rel-13 SC-PTM
  Introduction of necessary enhancements to support narrowband operation, e.g. support of NPDCCH, and coverage enhancement, e.g. repetitions
Using SIBs to convey all the multicast configuration is very inefficient and inflexible, especially when several different multicast services are ongoing at the same time.
It is beneficial to include assisting information in the multicast to assist the UE to decide whether to receive a certain multicast service.

## Slide 3: Proposal
One SC-MCCH per cell or NB-IoT anchor carrier is mapped on DL-SCH.
Use control-less semi-static scheduling for SC-MCCH and include information of TBS and MCS for SC-MCCH physical layer transmission in SIB20-NB.
Coverage related information can be send to the UE to facilitate the decision at the UE of receiving the multicast or not.
  FFS the exact mechanisms.