## Slide 1: Draft_WF on NB IoT SC-MTCH transmission
Ericsson …
R1-1610552
3GPP TSG RAN WG1 Meeting #86bis
Lisbon, Portugal, 10th – 14th Oct 2016
Agenda item 7.2.9.2

## Slide 2: Background
In NB-IoT’s Rel-14 WID, multi-cast downlink transmission is expected to be supported based on Rel-13 SC-PTM
  Introduction of necessary enhancements to support narrowband operation, e.g. support of NPDCCH, and coverage enhancement, e.g. repetitions
The amount of UEs that are listen to multicast can be large, and it is difficult to support PHY feedback from each UE.
Reliability of SC-MTCH transmission can be enhanced through combining between different transmissions.

## Slide 3: Proposal
No physical layer feedback is supported for SC-PTM in NB-IoT Rel14.
RAN1 studies the possibility of combining of multicast packages from different multicast occasions of the same multicast content.
RAN1 studies the possibility of combining erroneously received multicast package through unicast to enable the reliable reception of multicast service.