## Slide 1: WF on Sequence Collision in Uplink DMRS
Huawei, HiSilicon
3GPP TSG RAN WG1 Meeting #86bis R1-1610612
Lisbon, Portugal 10th - 14th October 2016
Agenda item - 7.2.2.3

## Slide 2: Background
Sequence collision may exist in the following cases:
DMRS with RPF=4 in cell 1 and legacy DMRS in cell 2
  Sequence collision between DMRS with RPF=4 and quarterly extracted sequence from legacy DMRS
  Sequence collision happens when is equal to .
DMRS with RPF=4 in cell 1 and DMRS with RPF=2 in cell 2
  Sequence collision between DMRS with RPF=4 and even elements extracted sequence from DMRS with RPF=2
  Sequence collision happens when is equal to .

## Slide 3: Proposal
Root sequence index for DMRS with RPF=2 is determined with 4*q, wherein, q is the root sequence index of legacy DMRS sequence in the cell.
Root sequence index for DMRS with RPF=4 is determined with 16*q, wherein, q is the root sequence index of legacy DMRS sequence in the cell.