## Slide 1: WF on SC-MCCH transmission for NB-IoT SC-PTM
Huawei, HiSilicon, ITL, [….]
R1-1610643
3GPP TSG RAN WG1 Meeting #86bis
Lisbon, Portugal, October 10-14, 2016
Agenda item 7.2.9.2

## Slide 2: Background
In NB-IoT’s Rel-14 WID, multi-cast downlink transmission is expected to be supported based on Rel-13 SC-PTM
  Introduction of necessary enhancements to support narrowband operation, e.g. support of NPDCCH, and coverage enhancement, e.g. repetitions
Scheduling and transmission method of SC-MCCH in NB-IoT SC-PTM needs to be determined.

## Slide 3: Proposals
The maximum number of on-going SC-MTCHs supported by SC-MCCH is reduced compared to LTE.
RAN1 assumes the maximum number of on-going SC-MTCHs supported by SC-MCCH is [64] in NB-IoT.
  Send LS to ask RAN2 confirm this number
One SC-MCCH can be segmented into multiple TBs when the number of configured SC-MTCHs results in SC-MCCH larger than can be conveyed by one TB;