## Slide 1: WF on Basics of LDPC Design
Ericsson, Intel, Qualcomm
R1-1610693
3GPP TSG RAN WG1 Meeting #86bis
Lisbon, Portugal, 10th-14th October 2016
Agenda item 8.1.3.1

## Slide 2: Background
Agreement in RAN1#85
  The Parity check matrix of Quasi-cyclic like LDPC Codes is defined at least by a matrix H of size (mb×z)×(nb×z), which consists of sub-block matrices of size z×z, where each sub-block matrix is composed by circularly shifted matrices or zero matrices.

## Slide 3: Proposal: IR support
In addition to (partial) Chase Combining, LDPC code design for NR provides rate-compatible IR HARQ support
  Code extension of a parity-check matrix is used for IR support
    Use diagonal extension
      Benefits:
        Low encoding complexity;
        No need of variable node update for VN of weight-1;
        No need to store extrinsic LLR for weight-1 VN, only channel LLR needed

## Slide 4: Proposal: Sub-blocks
Proposal:
  For the QC-LDPC design, the sub-blocks with circularly shifted matrices are circularly shifted ZZ identity matrices.

## Slide 5: Proposal: Highest Code Rate
Working assumption:
In parity check matrix design, the highest code rate to design H matrix for is
  4/5 <= Rmax <=8/9
  Rate matching to achieve transmission code rate higher than Rmax is not precluded
  Rmax is the highest code rate among all if multiple H matrices are designed