## Slide 1: WF on timing design for TTI bundling
CMCC
R1-1610697
3GPP TSG RAN WG1 Meeting #86bis
Lisbon, Portugal, October 10th – 14th, 2016
Agenda item 7.2.7

## Slide 2: Background
At the RAN1#86 meeting [1], the following agreements on Uplink Capacity Enhancements for LTE were achieved:
  Support TTI bundling for TDD configuration 2 and 3 when supporting of PUSCH in UpPTS
  Specify the scheduling and HARQ timing for TTI bundling as follows
    The UE shall upon detection of a PDCCH with DCI format 0 in subframe n intended for the UE, adjust the corresponding PUSCH transmission in subframe n+k, with k in the following table

## Slide 3: Proposals
Support TTI bundling for TDD configuration 2 and 3 when supporting of PUSCH in UpPTS
Specify the HARQ timing for TTI bundling as follows
  For scheduled PUSCH transmissions in subframe n, which corresponds to the last TTI in the bundle, a UE shall determine the corresponding PHICH resource in subframe n+k_phich, with k_phich in the following table
TDD UL/DL Config | DL subframe number n |  |  |  |  |  |  |  |  | 
 | 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9
2 |  | 7 | 6 |  |  |  | 7 | 6 |  | 
3 |  | 7 | 6 | 6 | 6 |  |  |  |  | 

## Slide 4: Proposals
Specify the scheduling and HARQ timing for TTI bundling as follows(cont’)
  The UE shall upon detection of a PHICH transmission intended for the UE in subframe n-l, adjust the corresponding first PUSCH transmission in the bundle in subframe n+k, with l in the following table
Specify the number of HARQ processes for subframe bundling operation under TDD configuration 2 and 3 as in the following table
TDD UL/DL Configuration | DL subframe number n |  |  |  |  |  |  |  |  | 
 | 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9
2 |  | 3 |  | 0 |  |  | 3 |  | 0 | 
3 | 1 |  |  |  |  |  |  | 7 | 0 | 1
TDD UL/DL configuration | Number of HARQ processes for subframe bundling operation
2 | 2
3 | 2