## Slide 1: Observations on hardware implementations of flexible channel decoders
3GPP TSG RAN WG1 Meeting #86bis R1-1610757
Lisbon, Portugal, 10th – 14th October 2016
Agenda Item: 8.1.3.1
AccelerComm, Orange, IMT, NEC, LG, Ericsson

## Slide 2: Background
From Chairman notes RAN1#86:
Conclusion:
The eMBB data channel coding scheme will be chosen at RAN1#86bis
  including agreeing on the observations that led to the decision.
Companies are encouraged to:
  continue analysis and comparison in order to inform the final decision at RAN1#86bis
  provide any remaining details, especially focusing on LDPC (in view of the situation in this meeting)
  provide any remaining details of the flexibility requirements and how they can be satisfied, and corresponding implementation complexity and any impact on performance

## Slide 3: Turbo codes
It is proposed that the following observations are captured:
Latency: Turbo codes, LDPC codes and polar codes can all achieve latencies of less than 16 μs The 90 nm turbo decoder of [1] in R1-1608584 can decode 6144 bits in 2.7 μs. By comparison, the 14 nm polar decoder of R1-1608865 has latencies of up to 9 μs.
Flexibility: The LTE turbo code and enhanced LTE turbo codes can meet the flexibility requirements of NR As discussed during AI 8.1.3.1 on 11th October 2016 and supported by R1-1610544
Implementation: For turbo decoders, there are concerns that implementation is challenging when targeting the highest throughput requirements of NR. As discussed during AI 8.1.3.1 on 11th October 2016