## Slide 1
WF on MIMO transmission based on multiple antenna panels
Huawei, HiSilicon, Xinwei, NEC, …
3GPP TSG RAN WG1 Meeting #86bis R1-1610893 Lisbon, Portugal, 10th - 14th Oct 2016
Agenda item: 8.1.4.2

## Slide 2: Proposals
Study at least the following different multi-panel structures at both TRP and UE
  Uniform panel array: antenna elements with the same polarization from multiple panels are uniformly distributed in horizontal and vertical dimensions respectively (see Fig.1(a))
  Non-uniform panel array: antenna elements with same polarization from multiple panels are not uniformly distributed in horizontal or vertical dimension (see Fig.1(b))
Study the non-coherent MIMO transmission based on multi-panel structures at TRP or UE
  Interference hypothesis and measurement
Study the coherent MIMO transmission based on non-uniform panel structure at TRP or UE
  Codebook design

## Slide 3: Appendix
dedge,H = dH, dedge,V = dV
dedge,H ≠ dH, dedge,V ≠ dV
Fig.1 Uniform and non-uniform antenna panel structures