## Slide 1: WF on Multiplexing of SYNC and Broadcast Signals
Qualcomm, CATT, […]
3GPP TSG RAN WG1 Meeting #86b
Lisbon, Portugal 10th – 14th October 2016
Agenda item: 8.1.5.1
R1-1610550

## Slide 2: Background
RAN1 recently agreement to following proposals in the recent meeting [1]
“RAN1 should strive for a common framework, including for example structure of synchronization signals, for initial access
More specifically, especially within a group of frequency bands in the frequency range, RAN1 should strive for an unified framework covering
  Single beam based and multi-beam based deployments
  TDD and FDD operations
  Different/mixed numerologies
  Standalone and non-standalone operations
RAN1 should take at least following requirements into account to design initial access
  Providing at least following functionalities
    Detection of NR cell and its ID
      Note: In this context, NR cell corresponds one or multiple TRP(s)
    Initial time/frequency synchronization to the cell
    Providing necessary information for random access
  Providing sufficient number of the identity values to allow deployment flexibility
  FFS: supporting efficient mobility
  FFS: supporting efficient inter-RAT measurement
  Reducing the frequency hypothesis UE needs to search for compared to LTE
  FFS: detecting beam ID(s)”
1. R1-167944, “WF on NR Initial Access”, 3GPP TSG RAN WG1 Meeting #86

## Slide 3: Multiplexing Options of SYNC and Broadcast Signals
As in the legacy LTE synchronization, the sync transmission should at least consist of
  A primary sync signal (PSS): to provide timing and frequency synchronization and some part of cell ID.
  A secondary sync signal (SSS): to provide the full cell ID and also some information about the sub-frame/frame index number.
Broadcast channel (PBCH) should provide the minimum system information required for initial UL transmission (may not include all information needed for serving cell selection)
There are different options for multiplexing PSS/SSS/PBCH: (a) TDM, (b) FDM, or (c) any combination of the two.

## Slide 4: FDM vs TDM of SYNC and Broadcast Signals
Aspect | TDM | FDM | comments
Subcarrier spacing (CP and duration of each sync sub-symbol) | Wider (shorter) | Narrower (longer) | 
Timing Estimation accuracy | Better | Worse | Finer TD samples in TDM approach
PAPR of PSS | Better | Worse | ZC-based PSS maintains good PAPR if not FDMed with other signals
PBCH demodulation | SSS used as the reference | Needs dedicated reference tones | TDM provides better resource utilization
Sensitivity to frequency offset/ phase noise | Less | More | 
Initial cell search complexity | Comparable |  | See note 1 of [2]
Neighbor cell search complexity (in async standalone mode) | Worse (4X) | Better | See note 1 of [2]
Frequency estimation accuracy | Better | Worse | See note 2 of [2]
Receive beam selection latency | Better | Worse | See note 3 of [2]
2. R1-1610159, “Multi-beam SYNC Design”, 3GPP TSG RAN WG1 Meeting #86b

## Slide 5: Proposal
NR supports the time division multiplexing of PSSS, SSS and PBCH signals in both sub-6 GHz and over-6 GHz band