## Slide 1: WF on TBS for FeMTC
Ericsson, Qualcomm, Sony
R1-1610663
3GPP TSG RAN WG1 Meeting #86bis
Lisbon, Portugal, 10th – 14th Oct 2016
Agenda item 7.2.8.1.1

## Slide 2: Background
RAN1#86 agreements:
  For Rel-14 FeMTC UEs, the maximum UL TBS for CEMode A UEs with maximum 1.4 MHz bandwidth in TDD/HD-FDD is increased to 2984 bits.
  For Rel-14 FeMTC UEs supporting larger UE channel BW for PDSCH and PUSCH:
    The larger max. DL TBS is at least 2984 bits.
    The larger max. UL TBS is at least 2984 bits.

## Slide 3: Proposal
Supported modulation schemes for FeMTC UEs:
  PDSCH: QPSK, 16QAM
  PUSCH: QPSK, 16QAM
Max TBS for 5-MHz FeMTC UE:
  PDSCH: [2984 or 4584 or 5160] bits
  PUSCH: [2984 or 4584 or 5160] bits
Soft buffer size for 5-MHz FeMTC UE:
  Option 1: N∙96∙⌈(X+28)/32⌉ where N = max number of DL HARQ processes and X = max DL TBS
  Option 2: a smaller value than in Option 1
Max UL TBS in CE mode A for 1.4-MHz FeMTC FD-FDD UE:
  Option A: 1000 bits (same as Rel-13 Cat-M1)
  Option B: 2984 bits (same as 1.4-MHz FeMTC TDD/HD-FDD UE)