## Slide 1
3GPP TSG RAN WG1 Meeting #86bis R1-1610845
Lisbon, Portugal, 11st - 14th Oct 2016
Agenda item: 8.1.5.3
WF on NR UL-based RRM Measurement
Huawei, HiSilicon, Qualcomm

## Slide 2: Background
The following agreements have been reached at RAN1#86:
  For RRM measurement in NR, at least DL measurement is supported with the consideration on
    Both single-beam based operation and multi-beam based operation
  FFS: Definition of RRM measurement for multi-beam based operation
  FFS: DL signal for RRM measurement
  FFS: When DL measurement is applied
  Note that there is no conclusion that DL measurement is a complete solution for RRM measurement in NR for now

## Slide 3: Background
The following agreements on new RAN controlled state have been reached at RAN2#94, #95 and RAN3#93:
  RAN2#94
    Study the introduction of a RAN controlled “state” characterised by, at least:
      UEs in RAN controlled state should incur minimum signalling, minimise power consumption, minimise resource costs in the RAN/CN making it possible to maximise the number of UEs utilising (and benefiting from) this state
      Able to start data transfer with low delay (as required by RAN requirements)
  RAN2#95
    RRC states with significantly overlapping characteristics should be avoided.
    At least one RRC state for low activity should meet the NR control plane latency requirement and must be capable of achieving comparable power efficiency to that of LTE’s IDLE state.
  RAN3#93
    In the inactive mode, the UE context is stored in RAN and UP data is buffered in RAN.

## Slide 4: Background
R1-1609437
  Observation 1: UL based measurements enable the TRP(s) selection within the NR cell.
  Observation 2: Configuring UL based measurement in dense network deployment result in efficient reduction on signalling overhead and UE power consumption.
  Observation 3: UL based measurement can alleviate the mobility interruption time and reduce the paging signalling overhead and HO failure rate, especially for high speed mobility and beam based operation scenarios.
  Observation 4: In RAN controlled state of low-frequency dense urban scenario, UL based RRM has better or close paging performance than DL based RRM with dynamic tracking area.
  Observation 5: DL based measurement should be support for L1/L2 beam management, and NR cell reselection for idle UE.

## Slide 5: Proposal
NR shall target to support UL-based RRM measurement and mobility at least in the following cases:
    New RAN Controlled State with low activity
    Active state L3 based NR handover
    Active state L1/2 based NR mobility