## Slide 1: WF on Multiplexing eMBB and URLLC in DL
Samsung, Panasonic, ZTE, ZTE Microelectronics, ETRI, Ericsson, CATT, Huawei, Docomo, LGE, CMCC, Convida wireless, InterDigital, Sony, Fujitsu
3GPP TSG RAN WG1 Meeting #86b
Lisbon, Portugal 10th – 14th October 2016
Agenda item: 8.1.2.2
R1-1610902

## Slide 2: Background
RAN1#86 Agreements:
  At least the following potential options should be considered
    At least for shorter transmission UL, semi-static resource sharing between URLLC and eMBB
      FDM and/or TDM manner
        UL grant-free transmission for URLLC
        Other schemes are not precluded
    Dynamic resource sharing between URLLC and eMBB
      For DL, mechanisms to schedule a transmission where the resources of it can overlap with resources of ongoing/scheduled longer transmission at least from network perspective
        FFS: A similar or same mechanism applicability to UL
        Preemption or superposition
        Other schemes are not precluded
      Scheduling based approaches (e.g., by adapting transmission duration or by using different subbands) to allow multiplexing of different durations of transmission
      UL grant-free transmission for URLLC
      Other schemes are not precluded
    Other mechanisms are not precluded

## Slide 3: Background
[R1-1608843] Overview of URLLC support for NR [Huawei, HiSilicon]
  Proposal1) FDM should be considered as a starting point to support URLLC and eMBB coexistence in same carrier.
  Proposal2) Support dynamic resource sharing for eMBB/URLLC coexistence in DL.
  Proposal3) Support semi-static resource sharing for eMBB/URLLC coexistence in UL.
  Proposal4) Support frame structure where one URLLC slot contains 7 symbols with 60 kHz SCS.
[R1-1609546] On eMBB and URLLC multiplexing [Intel Corporation]
  Proposal) Study synchronous listen-before-talk mechanisms for dynamic eMBB and URLLC multiplexing
[R1-1610188] URLLC system capacity and URLLC/eMBB multiplexing efficiency analysis [Qualcomm Incorporated]
  Proposal2) NR should consider dynamic multiplexing of eMBB and URLLC services in both FDM and TDM fashion over the system bandwidth.

## Slide 4: Proposal
From network perspective, eMBB and URLLC multiplexing in DL is supported by
  Using same sub-carrier spacing
  Using different sub-carrier spacing
    Using same and/or different CP overheads
  Both approaches are supported
NR should ensure efficient dynamic resource sharing between eMBB and URLLC in DL