## Slide 1: WF on IMR types for NR
LG Electronics, Ericsson, Intel, InterDigital, KT, [CATT], [Qualcomm], xxx
R1-1703567
3GPP TSG RAN1 #88
Athens, Greece, Feb. 13 – 17, 2017
Agenda Item: 8.1.2.3.5

## Slide 2: Background
In RAN1 NR adhoc, following agreement was made.
  Agreements:
    For NR, support at least two types of resources used for interference measurement in CSI configuration based on the following candidates:
      ZP CSI-RS, NZP CSI-RS, DMRS
        Including independent or joint usage of any combination of the above three candidates
      Selection is to be done in RAN1#88

## Slide 3: Proposal
NR supports both ZP CSI-RS and NZP CSI-RS based interference measurement.
  FFS: supporting DMRS for IMR
  ZP CSI-RS RE patterns may be different from NZP CSI-RS RE patterns
    FFS: ZP CSI-RS overlapped with other RSs (e.g. DMRS)
Support interference measurement based solely on ZP CSI-RS
Support both or one of followings
  Interference measurement based solely on NZP CSI-RS
  Interference measurement based on joint usage of ZP CSI-RS and NZP CSI-RS
Interference method can be continued to discuss in WI phase
  Alt1: interfere estimation channel coefficient/covariance estimation
  Alt2: interference power estimation
  Alt3: subtraction of the estimated desired signal
  Others not precluded
  Note: this does not mandate UE implementation and specification