## Slide 1: WF on remaining issues on advanced CSI reporting
Samsung, Ericsson, LG Electronics, Xinwei, NTT DOCOMO, ….
3GPP TSG RAN WG1 Meeting #88
Athens, Greece 13th - 17th February 2017
Agenda item: 7.2.2.6
R1-1703645

## Slide 2: Proposal: for advanced CSI
For A-CSI, support PUSCH mode 1-2, 2-2, 3-1, and 3-2
For P-CSI, support only PUCCH mode 1-1
  For RI=1,2 CQI/PMI is calculated based on advanced CSI codebook
  For RI>2, CQI/PMI is calculated based on legacy/class A codebook (see next slide)
  Based on PUCCH Format 2/2A/2B
  3 reporting instances (analogous to Rel.13 Class A)
    1st reporting instance: RI + beam power
    2nd reporting instance: (i1,1,i1,2)
    3rd reporting instance: i2 / CQI
      For rank 1, i2 is 6 bits (not subsampled)
      For rank 2, i2 is 4 bits, with , where (2 bits) is QPSK, and (1 bit) and (1 bit) are BPSK

## Slide 3: Proposal: for advanced CSI
For rank 3-8 P-CSI and rank 3-8 A-CSI, use following codebooks
  4 port: Rel. 8/12 4 Tx rank 3-4 codebook
  8 port, 1D: Rel. 10 8 Tx rank 3-8 codebook
  8 ports, 2D: Rel. 13 rank 3-8 Class A codebook
  {12,16,20,24,28,32} ports: Rel. 13/14 rank 3-8 Class A codebook
(N1,N2) combinations
  Support all Rel. 13/14 Class A combinations
  Support two additional combinations, (N1,N2) = (2,1) and (4,1)
Use Class A RRC parameter to configure codebook parameters
  (N1,N2)
  (O1,O2,Config) only for Class A (N1,N2) combinations and rank 3-8