## Slide 1: WF on QCL for CSI-RS
3GPP TSG RAN WG1 Meeting #88 R1-1703530
Athens, Greece, 13th –17th February 2017
Agenda Item: 8.1.2.4.5
ZTE, ZTE Microelectronics,

## Slide 2: Background
  Regarding QCL indication for CSI-RS, it has been agreed that
  Indication of QCL between the antenna ports of two CSI-RS resources is supported.
    By default, no QCL should be assumed between antenna ports of
    two CSI-RS resources.
    Partial QCL parameters (e.g., only spatial QCL parameter at UE
    side) should be considered.
  For downlink, NR supports CSI-RS reception with and without beam-related indication,
    When beam-related indication is provided, information pertaining
    to UE-side beamforming/ receiving procedure used for CSI-RS-
    based measurement can be indicated through QCL to UE
    QCL information includes spatial parameter(s) for UE side
    reception of CSI-RS ports
        FFS: information other than QCL

## Slide 3: Proposal
  Indication of partial QCL parameters between two QCL between the antenna ports of two CSI-RS resources is supported
    Which of the partial QCL parameters are configured by gNB