## Slide 1: WF on Dynamic Signaling for CSI-RS Activation
Samsung, Qualcomm, Intel Corporation, NTT DOCOMO, …
3GPP TSG RAN WG1 88
Athens, Greece 13th - 17th Feb. 2017
Agenda item: 8.1.2.3.1
R1-1703604

## Slide 2: Background
The following was agreed in RAN1 NR-AH 2017-01:
  For periodic CSI-RS,
    Semi-persistent CSI reporting is activated/deactivated by MAC CE and/or DCI
    Aperiodic CSI reporting is triggered by DCI
      FFS: Necessity of additional signaling with MAC CE
  For semi-persistent CSI-RS,
    Periodic CSI reporting is not supported.
    Semi-persistent CSI reporting is activated/deactivated by MAC CE and/or DCI
      Semi-persistent CSI-RS is activated/deactivated by MAC CE and/or DCI
      FFS: Relationship of signaling between CSI reporting and CSI-RS transmission
    Aperiodic CSI reporting is triggered by DCI
      Semi-persistent CSI-RS is activated/deactivated by MAC CE and/or DCI
      FFS: Necessity of additional signaling with MAC CE
  For aperiodic CSI-RS,
    Periodic [and semi-persistent] CSI reporting is not supported
    Aperiodic CSI reporting is triggered by DCI
      Aperiodic CSI-RS is triggered by DCI and/or MAC CE
      FFS: Relationship of signaling between CSI reporting and CSI-RS transmission, e.g., common DCI signaling between CSI reporting and CSI-RS transmission
      FFS: Necessity of additional signaling with MAC CE
  Note that further down selection can be done later between MAC CE and DCI in above bullets
  …

## Slide 3: Proposal
When a UE is configured with K NZP CSI-RS resources (resource sets) in a Resource setting
  Activation of N out of K (1 ≤ N ≤ K) NZP CSI-RS resources (resource sets) is signaled via MAC CE
The above activation mechanism (selecting N out of K NZP CSI-RS resources) is used for aperiodic (AP) and semi-persistent (SP) CSI-RS
  Analogous to Rel.14 LTE
  For AP-CSI-RS, 1 out of the N CSI-RS resources is selected via DCI signaling
    FFS: Whether DCI used for CSI-RS resource selection is the same as that for A-CSI triggering