## Slide 1: WF on Aperiodic CSI-RS Resource Selection
Huawei, HiSilicon, Nokia, Alcatel-Lucent Shanghai Bell, Qualcomm, CATT, LG Electronics
3GPP TSG RAN WG1 #88 R1-1703672
Athens, Greece, 13th – 17th February 2017
Agenda item: 7.2.2.2

## Slide 2: Background
Conclusion from RAN1#86bis:
3 alternatives are identified:
  Alt1 Reuse A-CSI request field and add more bit(s) if necessary
  Alt2 Reuse CS field (see R1-1610815, R1-1610816)
  Alt3 Add ceil(log2(N))-bit or 2-bit DCI field
Decide between the above 3 alternatives.
  Aperiodic CSI-RS resource selection was not touched in RAN1 #87 due to time limitation

## Slide 3: Proposal
For aperiodic CSI-RS resource selection, the existing A-CSI request field is reused with additional B bits
  B = 0 (only if N=1), 2 configured by higher layer signaling
  Each state of the triggering fields corresponds to a set of combination of {CSI process, CSI-RS resource}
    If MAC CE is not used to activate CSI-RS resource for a CSI process, the CSI-RS resource in the {CSI process, CSI-RS resource} corresponds to the aperiodic CSI-RS resource configured by RRC signaling
    Otherwise the CSI-RS resource in the {CSI process, CSI-RS resource} corresponds to the aperiodic CSI-RS resource activated by MAC CE
  The additional B bits are added to the A-CSI request field for DCI formats 0 and 4 mapped onto the UE specific search space given by the C-RNTI