## Slide 1: WF on RACH preamble format
Samsung, ZTE , ZTE Microelectronics, Ericsson, NTT DOCOMO
3GPP TSG RAN WG1 #88
Athens, Greece, 13th – 17th February 2017
Agenda item: 8.1.1.4.1

## Slide 2: Background
Agreement:
  For single/multi-beam operation,
    For multiple/repeated RACH preamble transmissions, consider only option 1, option 2 and option 4
      Option 1: CP is inserted at the beginning of the consecutive multiple/repeated RACH OFDM symbols, CP/GT between RACH symbols is omitted and GT is reserved at the end of the consecutive multiple/repeated RACH symbols
      Option 2/4: The same/different RACH sequences with CP is used and GT is reserved at the end of the consecutive multiple/repeated RACH Preamble
        Study:
          Multiplexing with different orthogonal cover codes
          Independent RACH sequences in a RACH preamble
  For supporting various coverage and forward compatibility, flexibility in the length of CP/GT and the number of repeated RACH preambles and RACH symbols is supported
  Note: specific use of these three options may depend on RACH subcarrier spacing and TRP beam correspondence
Agreement:
  NR defines that:
    a random access preamble format consists of one or multiple random access preamble(s),
    a random access preamble consists of one preamble sequence plus CP, and
    one preamble sequence consists of one or multiple RACH OFDM symbol(s)
  UE transmits PRACH according to the configured random access preamble format

## Slide 3: Proposal
NR at least supports option 1, and consider option 1 as baseline for comparison with other options.
  For RACH capacity enhancements and/or conveying DL Tx beam ID,
    Option 2 with OCC and/or option 4 with different sequences can be considered.
      Note: for option 4, combination with different sequences can be studied
      Note: for option 4, two-stage or multiple-stage UE detection can be studied for possible complexity reduction for PRACH detection
    Other schemes are not precluded
  FFS : Number of Preambles/Symbols, Length of CP/GT
The region for PRACH transmission should be aligned to the boundary of uplink symbol/slot/subframe