## Slide 1
3GPP TSG RAN WG1 NR Ad-Hoc Meeting R1-1704009 Athens, Greece, 13th - 17th February 2017
Agenda item: 8.1.2.5
WF on analysis of nonlinear precoding
Mitsubishi Electric, InterDigital, IITH, CeWiT, IITM, Tejas Networks, KDDI, AT&T, Huawei, HiSilicon, Nokia, Alcatel-Lucent Shanghai Bell, [NTT DOCOMO]

## Slide 2: Background
  In the RAN1#86b meeting, the following agreement was made [1]
  Study performances of nonlinear precoding schemes for MU-MIMO focusing on the following aspects
  Potential nonlinear precoding schemes
  Performance advantages over linearly precoded systems
  Comparison of complexity with respect to linearly precoded systems
  specification Impacts (e.g., signaling and RS design, etc.)
  In this WF, more detailed study topics are proposed based on the observations and proposals made in contributions.
[1] R1-1610831 WF on Spatial Multiplexing Schemes for MU-MIMO, Mitsubishi Electric, InterDigital, Samsung, NTT DOCOMO, IITH, IITM, Tejas Networks, CEWIT, KDDI, also supported by AT&T, Reliance jio, Huawei, HiSilicon

## Slide 3: Background (R1-1701457)
Based on the observations made in the contributions, more details are added in the study:
At least the following schemes are considered for the study
  nonlinear precoding (NLP) schemes, e.g., Tomlinson-Harashima precoding, vector perturbation
  hybrid precoding schemes (e.g., semi-dynamic or dynamic switching between linear precoding and NLP)
Consider the following evaluation assumptions:
  MU-MIMO DMRS in R1-1700480, multiple access in TR38.802, COMP coherent joint transmission, other evaluation assumptions are not precluded
Consider the following issues related to performance evaluation
  Abstraction methods for SLS, channel estimation error modeling, etc
Study the impact of the following impairments/implementation aspects on NLP:
  Channel estimation error, CSI feedback error, SRS reciprocity error, ordering process of users at transmitter, receiver implementation, complexity of implementation of NLP, etc.
Study spec impact including following:
  Signaling methods for NLP: indication of filter types, indication of use of linear/nonlinear precoding, etc.
  DMRS designs for NLP
  Other studies on spec. impact are not precluded

## Slide 4: Background: summary of observations (from NR Ad-hoc in Jan. 2017 and RAN1#88)
[2] R1-1701678, “Non-linear Precoding for Downlink Multiuser MIMO,” Huawei, HiSilicon, Athens, Greece, Feb. 2017
[3] R1-1700711, “Non-linear precoding for NR,” InterDigital, Spokane, USA, Jan. 2017
[4] R1-1702848, “Non-linear precoding for NR,” NTT DCOMO, Athens, Greece, Feb. 2017
[5] R1-1703186, “Nonlinear Precoding for Interference Mitigation in HetNets,” Nokia, Alcatel-Lucent Shanghai Bell, Athen, Greece, Feb. 2017
[6] R1-1703187, “On MU MIMO non-linear precoding in NR,” Nokia, Alcatel-Lucent Shanghai Bell, Athens, Greece, Feb. 2017
[7] R1-1702754, “Summary of analysis of nonlinear precoding schemes for NR,” Mitsubishi Electric, Athens, Greece, Feb. 2017
[8] R1-1700873, “Views on abstraction techniques of nonlinear precoding schemes for SLS,” Mitsubishi Electric, Spokane, USA, Jan. 2017
[9] R1-1702753, “MU-MIMO performance evaluation of nonlinear precoding schemes,” Mitsubishi Electric, Athens, Greece, Feb. 2017
[10] R1-1703490, “Field Results of Multi TRP transmission using non-linear THP,” IITH, CEWiT, IITM, Tejas Networks, Athens, Greece, Feb. 2017
Precoding schemes considered in contributions
Tomlinson Harashima Precoding (THP) based schemes [2, 3, 4, 5, 6, 7]
Vector perturbation based schemes [3, 4]
Hybrid approach (combination of LP and NLP) [4, 6]
Performance evaluation related issues and performance evaluation results
CSI estimation error model [6]
Abstraction methods of SLS [4, 6, 8]
Complexity analysis, impact of modulo operation, sensitivity to CSI estimation error [6]
Throughput performance evaluation results：Rayleigh fading channel model [2], WINNER II local area small office [6], LLS MU-MIMO [9], CoMP/CRAN field trial [10]
Issues related to specification impact
Signaling of linear precoding (LP) types, CSI feedback schemes, receiver processing [2]
Signaling to enable dynamic switching between LP and non-liner precoding (NLP) schemes, processing procedures between DMRS and data for NLP, RS design [4]
CSI reporting/acquisition mechanism, use prescheduling, CSI estimation improvement, content, timing and frequency of CSI feedback, reciprocity based CSI acquisition [5, 6]
Signalling precoder types (LP or NLP) [7]
Performance impairment factors
Channel estimation error, ordering of users at transmitter [3, 4]
Quality of CSI feedback, amount of CSI feedback [5]
Possible areas of applications of NLP
HetNet [5], MU-MIMO [2, 3, 4, 6, 7], CoMP/CRAN [10],

## Slide 5: Background: Example of linear and nonlinear hybrid precoding
R1-1703187
R1-1702848

## Slide 6: Proposals
Based on the result of the study, the following proposals are made:
In NR, transmitter side interference cancellation techniques for co-scheduled UEs are considered
NR identifies nonlinear precoding as one of the transmitter side interference cancellation techniques
NR considers the following nonlinear precoding techniques
  DPC based precoding techniques (e.g., Tomlinson Harashima precoding, QL based DPC, ZF-THP), vector perturbation
  Linear and nonlinear hybrid precoding techniques