## Slide 1: WF on UL Mobility Evaluation Results
Qualcomm, Huawei, Hi-Silicon, Sony
3GPP TSG RAN WG1 Meeting #88
Athens, Greece 13th - 17th February 2017
Agenda item 8.1.1
R1-1704097

## Slide 2: Background
The following online observation has been made on UL base mobility performance
  UL measurements for mobility have been studied by RAN1 and the following observations were made compared to LTE DL measurement baseline with 5 ms SS periodicity and CRS:
    For CONNECTED_ACTIVE state, following observations were made by some companies:
      In synchronized deployment, UL measurements can provide a handover performance and / or potential UE power consumption gain in some scenarios with a potential cost of increased UL resource and potential NW backhaul signaling overhead depending on NW architecture and potential reduction in over the air signaling overhead, e.g. dense deployments with low number of UE’s per TRP, high speed
    For CONNECTED_INACTIVE state, following observations were made by some companies:
      In synchronized deployment, UL measurements with synchronization signals transmitted in SFN mode can provide a paging reliability performance and / or UE power consumption gain in some scenarios with a cost of increased UL resource and potential NW backhaul signaling overhead depending on NW architecture and potential reduction in over the air signaling overhead, e.g. dense deployments, rural high way

## Slide 3: Proposal
Capture slides 4, 5, 6 and 7 into Section 9.1.x of TR 38.802

## Slide 4: Table 1: Power Consumption in RRC Connected Active
Source 2 (R1-1703130) |  | 
Scenario | mobility scheme | UE Power Consumption
200m ISD with 3km/hr UE with DRX | DL measurement based mobility (40ms DRX cycle) | 4.69mW
 | UL measurement based mobility (80ms DRX cycle) | 2.65mW
200m ISD with 120km/hr UE with DRX | DL measurement based mobility (40ms DRX cycle) | 6.44mW
 | UL measurement based mobility (80ms DRX cycle) | 2.65mW
200m ISD with 3km/hr UE without DRX | DL measurement based mobility | 23.5mW
 | UL measurement based mobility (80ms UL SRS period) | 23.6mW
200m ISD with 120km/hr UE without DRX | DL measurement based mobility | 25.3mW
 | UL measurement based mobility (80ms UL SRS period) | 23.6mW

## Slide 5
 |  | Paging Miss Probability |  | 
Deployment Scenario | Mobility Schemes | Source 1 |  | Source 2
 |  | R1-1702595 | R1-166393 | R1-1609437
Rural with 120km/hr UE | DL Measurement Based Mobility | 4% |  | 
 | DRX cycle (0.32seconds) |  |  | 
 | DL Measurement Based Mobility | 8% |  | 
 | DRX cycle (1.28seconds) |  |  | 
 | UL Measurement Based Mobility | 3% |  | 
 | DRX cycle (1.28seconds) |  |  | 
Dense Urban with 30km/hr UE | DL Measurement Based Mobility | 12% |  | 
 | DRX cycle (0.16seconds) |  |  | 
 | DL Measurement Based Mobility | 26% |  | 
 | DRX cycle (1.28seconds) |  |  | 
 | UL Measurement Based Mobility | 6% |  | 
 | DRX cycle (1.28seconds) |  |  | 
 | DL Measurement Based Mobility |  | 2% | 16%
 | DRX cycle (0.375seconds) |  |  | 
 | DL Measurement Based Mobility |  | 8% | 32%
 | DRX cycle (1.5 seconds) |  |  | 
 | UL Measurement Based Mobility |  | 1% | 1%
 | DRX cycle (1.5 seconds) |  |  | 
High speed train with 480km/hr UE | DL Measurement Based Mobility |  | 8% | 
 | DRX cycle (0.375seconds) |  |  | 
 | DL Measurement Based Mobility |  | 3% | 
 | DRX cycle (1.5 seconds) |  |  | 
 | UL Measurement Based Mobility |  | 2% | 
 | DRX cycle (1.5 seconds) |  |  | 
Table 2: Paging Miss Probability in RRC Connected Inactive

## Slide 6: Table 3: Power Consumption in RRC Connected Inactive
Source 1 (R1-1702595) | 
 | UE Power Consumption (mA @ Battery)
UL Measurement Based Mobility All Scenarios | 2.0
DL Measurement Based Mobility Benign Mobility (semi-static UE) | 1.8
DL Measurement Based Mobility Rural with 120km/hr UE | 4.2
DL Measurement Based Mobility Dense Urban with 30km/hr UE | 7.9

## Slide 7: Observations
  UL measurements for mobility have been studied by RAN1 and the following observations were made compared to LTE DL measurement baseline with 5 ms SS periodicity and CRS:
    For CONNECTED_ACTIVE state, following observations were made by some companies:
      In synchronized deployment, UL measurements can provide a handover performance and / or potential UE power consumption gain in some scenarios with a potential cost of increased UL resource and potential NW backhaul signaling overhead depending on NW architecture and potential reduction in over the air signaling overhead, e.g. dense deployments with low number of UE’s per TRP, high speed
    For CONNECTED_INACTIVE state, following observations were made by some companies:
      In synchronized deployment, UL measurements with synchronization signals transmitted in SFN mode can provide a paging reliability performance and / or UE power consumption gain in some scenarios with a cost of increased UL resource and potential NW backhaul signaling overhead depending on NW architecture and potential reduction in over the air signaling overhead, e.g. dense deployments, rural high way