## Slide 1: WF on non-codebook based transmission for UL
LG Electronics, CATT, Ericsson, Huawei, HiSilicon
R1-1706445
3GPP TSG RAN1 #88bis
Spokane, USA, 3rd – 7th April 2017
Agenda Item: 8.1.2.1.4

## Slide 2: Agreements in RAN1#88

## Slide 3: Proposals
Non-codebook based transmission for UL is supported at least by following signaling in UL grant:
  SRI without TPMI/TRI, where
    Rank is the same as the sum of the configured number of SRS ports across one or multiple selected SRS resource(s) by the SRI.
    For data transmission, UE should apply the same precoder(s) for PUSCH port(s) as used in the SRS port(s) indicated by the SRI.
    FFS: additional indication on selection of multiple SRS resources for supporting frequency-selective precoding