## Slide 1
3GPP TSG RAN WG1 Meeting #88bis R1-1706809
Spokane, USA, April 3rd -7th, 2017
Agenda item: 8.1.2.3.3
WF on Schemes of Partial Channel Reciprocity
Huawei, HiSilicon, Samsung, MediaTek

## Slide 2: Background
The following agreements were achieved in RAN1 88
Update the RAN1 Jan. Ad hoc agreements as follows;
  Study the following DL CSI feedback for different degree of channel reciprocity,
    For full channel reciprocity
      Explicit interference feedback: e.g., Interference covariance matrix, diagonal elements of interference covariance matrix
      Implicit interference feedback: e.g., Interference PMI feedback
      Explicit channel feedback: e.g., CSI of multiple TRPs
    For partial channel reciprocity (e.g., more Rx ports than Tx ports at UE)
      Partial CSI feedback for eNB to acquire full CSI
    Non-PMI feedback (legacy: eNB send beamformed RS, and UE report RI/CQI)
      CSI contains RI and CQI
      FFS how RI and CQI are derived
        E.g., RI and CQI depend on a PMI which is selected from a defined codebook or a configured codebook subset
        UE may also calculate RI and CQI directly with estimated channel without assuming PMI from any predefined codebook, FFS spec impact
  Study whether or not to support CSI-RS and SRS transmission in the same slot (e.g., for fast CSI acquisition)
    Study if a limitation on the number of SRS and/or CSI-RS ports due to UE complexity, slot duration of different numerology are needed.

## Slide 3: Proposal
For the case of partial channel reciprocity (i.e. less Tx ports than Rx ports at UE), study and evaluate at least the following candidate schemes
  Scheme 1 (Baseline): Non-PMI feedback
  Scheme 2: Partial CSI feedback for gNB to acquire full CSI
    Partial CSI is the information of the partial DL channel (e.g. partial DL channel vector/matrix or partial DL channel covariance matrix) with no reciprocal UL transmission due to the absence of Tx ports corresponding to the Rx ports at UE
  Scheme 3: CSI feedback with non-precoded/beamformed CSI-RS including CQI, RI and PMI
    For beamformed CSI-RS, precoding matrix is determined from CSI available at base station from SRS transmission
    PMI could be for a linear combination codebook
  Scheme 4: SRS switching
    SRS switching is used to obtain full channel information by multiple SRS transmission instants. Non-PMI CSI feedback can be used along with SRS switching
  Combination of the above schemes can be considered
  Note: both performance and overhead should be considered when comparing the above schemes
Simulation parameters are provided on the following slide
  Companies describe the assumed UL-DL calibration model
Companies are encouraged to provide the simulation results in next meeting

## Slide 4
Parameters | Values
Duplex mode | TDD
Carrier frequency | 2GHz
Simulation bandwidth | 10MHz
Channel model | 3D UMI / UMA
gNB antenna configuration | (M, N, P, Mg, Ng) = (8, 8, 2, 1, 1); (dH, dV) = (0.8, 0.5)λ Other configurations can be considered.
gNB TXRU mapping | (MTXRU, NTXRU, P, Mg, Ng) = (2, 4, 2, 1, 1), (1, 4, 2, 1, 1), (1, 2, 2, 1, 1) Other configurations can be considered
UE antenna configuration | 1Tx2Rx, 1Tx4Rx, 2Tx4Rx, Cross-polarized with 0, 90deg Other configurations can be considered Each company provides its deployment assumption
UE receiver noise figure | 9dB
UE antenna gain | Follow TR 36.873
Traffic model | Non-Full buffer, FTP model 1, 0.5MB packet size
UE distribution | 80% Indoor, 20% Outdoor
Scheduler | PF
HARQ scheme | Maximum 3 retransmissions
UE receiver type | MMSE-IRC
Channel estimation | Non-ideal -Note: for channel estimation from SRS and/or CSI-RS
UL-DL calibration | Ideal, non-ideal (each company describes the assumed UL-DL calibration model)
MIMO mode | MU-MIMO with rank adaptation