## Slide 1: WF on Triggering Mechanism for CSI Reporting
NTT DOCOMO, InterDigital, Intel, LGE, Sharp, CATT
R1-1706505
3GPP TSG RAN WG1 Meeting #88bis
Agenda item: 8.1.2.3.1

## Slide 2: Background
Agreements (in NR-adhoc #1):
For periodic CSI-RS,
  Semi-persistent CSI reporting is activated/deactivated by MAC CE and/or DCI
  Aperiodic CSI reporting is triggered by DCI
    FFS: Necessity of additional signaling with MAC CE
For semi-persistent CSI-RS,
  Periodic CSI reporting is not supported.
  Semi-persistent CSI reporting is activated/deactivated by MAC CE and/or DCI
    Semi-persistent CSI-RS is activated/deactivated by MAC CE and/or DCI
    FFS: Relationship of signaling between CSI reporting and CSI-RS transmission
  Aperiodic CSI reporting is triggered by DCI
    Semi-persistent CSI-RS is activated/deactivated by MAC CE and/or DCI
    FFS: Necessity of additional signaling with MAC CE
For aperiodic CSI-RS,
  Periodic [and semi-persistent] CSI reporting is not supported
  Aperiodic CSI reporting is triggered by DCI
    Aperiodic CSI-RS is triggered by DCI and/or MAC CE
    FFS: Relationship of signaling between CSI reporting and CSI-RS transmission, e.g., common DCI signaling between CSI reporting and CSI-RS transmission
    FFS: Necessity of additional signaling with MAC CE
Note that further down selection can be done later between MAC CE and DCI in above bullets
Note that it is possible to dynamically trigger RS and reports through links in the measurement setting

## Slide 3: Background
Agreements (in NR-adhoc #1):
NR supports mechanism(s) to trigger aperiodic CSI-RS and aperiodic CSI reporting simultaneously.
  FFS: signaling details (e.g. single DCI or separate DCI)
  FFS: method(s) for interference measurement
  FFS: reference resource of aperiodic CSI reporting
For aperiodic CSI-RS timing offset X, support X=0 at least, if aperiodic CSI-RS triggering is done by DCI
  FFS: supporting other values of X
  Note: ‘aperiodic CSI-RS timing offset X’ refers to the time gap between aperiodic CSI-RS triggering and aperiodic CSI-RS transmission w.r.t. number of slots.
For CSI reporting timing offset Y that is fixed or configurable by the network but with certain restriction on lower limit of Y to provide sufficient CSI computation time.
  Candidate values of Y are fixed or pre-determined by certain rule(s).
    Rule is FFS (e.g. number of CSI measurement/RS/reporting settings, CSI feedback type, number of ports, nearest CSI-RS transmission timing, UE capability, etc.)
  Note: ‘aperiodic CSI reporting timing offset Y’ refers to the time gap between aperiodic CSI reporting triggering and aperiodic CSI reporting w.r.t. number of slots.
  FFS Y is fixed or configurable
  FFS configuration is done by DCI and/or MAC CE and/or higher layer signaling

## Slide 4: Background
Stable items
TBD items
 |  | CSI reporting |  | 
 |  | Periodic | Semi-persistent | Aperiodic
CSI-RS transmission | Periodic | CSI-RS: N/A Reporting: N/A | CSI-RS: N/A Reporting: MAC CE | CSI-RS: N/A Reporting: DCI
 | Semi-persistent | Not supported | CSI-RS: MAC CE Reporting: MAC CE | CSI-RS: MAC CE Reporting: DCI
 | Aperiodic | Not supported | FFS | CSI-RS: DCI Reporting: DCI

## Slide 5: Proposal
Semi-persistent CSI reporting is not supported for aperiodic CSI-RS.

## Slide 6: Proposal
Semi-persistent CSI-RS is activated/deactivated by MAC CE.
  FFS: Additional DCI signaling in case for aperiodic CSI reporting (e.g., scheme in Appendix)
Semi-persistent CSI reporting is activated/deactivated by MAC CE.

## Slide 7: Appendix
Hybrid triggering mechanism for semi-persistent CSI-RS and aperiodic CSI reporting
Semi-persistent CSI-RS deactivated
Semi-persistent CSI-RS activated
0  No reporting
0  No report
1  Aperiodic report
1  Aperiodic report
Activation/deactivation
DCI signaling
MAC CE signaling