## Slide 1: Way forward on coverage in NB-IoT small cell
Ericsson
R1-1709218
3GPP TSG RAN WG1 Meeting #89
Hangzhou, China, May 15-19, 2017
Agenda item 6.2.7.4

## Slide 2: Background
In RAN#75, Further NB-IoT enhancements WI is introduced (see RP-170852).
Introducing support of small cell is part of the WID as follows.
  NB-IoT small cell support
  Specify necessary support for NB-IoT to be used in microcell, picocell, and femtocell deployments [RAN4, RAN2, RAN1].
    Appropriate eNB classes [RAN4]
    Support for closed subscriber group (CSG) functionality can be considered. [RAN2]
In RAN1#88bits, it is suggested to study the impact on RAN1 of introducing small cells.

## Slide 3: Background
The small cell eNBs have much lower output power than macro eNBs.
The coverage due to low eNB output power can be compensated by increasing the number of repetitions. But using a larger number of repetitions in the DL results in the DL throughput is too low to sustain services from higher layers.
In the UL, the receiver at the small cell eNBs usually have much higher noise figure comparing to macro eNBs. This results in a loss of coverage, which cannot be compensated by the current UL design.
BS output power and NF:
  Wide area BS: 46 dBm inband, 43 dBm standalone, 5 dB NF
  Medium range BS: 38 dBm, 8 dB NF
  Local area BS: 24 dBm, 13 dB NF

## Slide 4: Proposal
  The small cell MCL should be relaxed by the maximum of {reduction of base station output power, increase in base station noise figure} compared to Wide Areas BS.

## Slide 5: Proposed conclusions
No RAN1 impacts are identified from the coverage point of view of NB-IoT small cell, i.e., there is no needs to increase the number of repetitions in the DL and UL.
FFS other aspects of small cells to identify possible RAN1 impacts.
Send a LS to RAN4 to inform them about the proposed agreement and conclusions.