## Slide 1: WF on NR-SS sequence design
NTT DOCOMO, ZTE
3GPP TSG RAN WG1 Meeting #89 R1-1709220
Hangzhou, China
15th – 19th May, 2017
Agenda item: 7.1.1.1.1
Document for decision

## Slide 2: Background
Agreements:
Working assumption: Number of PSS sequences: 3
  PSS sequence details:
    Frequency domain-based pure BPSK M sequence (fixing the time/freq. offset ambiguity)
      1 polynomial: octal 145 Decimal 145 (i.e. g(x) = x7 + x4 + 1)
      In freq. domain 3 cyclic shifts (0, 43, 86) to get the 3 PSS signals
      Initial poly shift register value: 1110110
    FFS modified ZC: 2 ZC sequences concatenation or interleaving in time or freq., 4 ZC sequences concatenation in time
Number of SSS signals: 1000 post-scrambling
PSS sequence length: 127 for frequency domain-based pure BPSK M sequence
  Note that PSS will be mapped to consecutive 127 subcarriers
SSS sequence length: 127
Subcarrier spacings for PSS/SSS for difference freq. ranges: 15kHz/30kHz for below 6 GHz, and 120kHz/240kHz for above 6 GHz
  Note: RAN1 assumes that RAN4 will decide it depending on frequency ranges
SSS sequence details: Long M-sequence with scrambling

## Slide 3: Proposal
Confirm following working assumptions on NR-PSS as agreements
  Number of PSS sequences: 3
    PSS sequence details:
      Frequency domain-based pure BPSK M sequence (fixing the time/freq. offset ambiguity)
        1 polynomial: Decimal 145 (i.e. g(x) = x7 + x4 + 1)
        In freq. domain 3 cyclic shifts (0, 43, 86) to get the 3 PSS signals
        Initial poly shift register value: 1110110

## Slide 4: Proposal
Down select NR-SSS sequence design from following options
  Option 1: 1 polynomial with 127 cyclic shifts, and 1 another polynomial with 9 cyclic shifts
    Two generator polynomials will be defined for m-sequences, and cyclic shift according to NR-cell ID is applied to each m-sequence
    See appendix A for detailed example
  Option 2: 3 polynomials with 127 cyclic shifts, and 1 another polynomial with 3 cyclic shifts
    Three generator polynomials will be defined for m-sequences, and one out of three is selected and cyclic-shifted according to the part of NR-cell ID
    One additional generator polynomial will be defined for scrambling sequence, and cyclic shift according to PSS ID is applied to generated scrambling-sequence
    See appendix B for detailed example

## Slide 5: Appendix A
Option 1:
  two M-sequences and are given by preferred pair of polynomials
    For example,
      , and for
  Cyclic shift given by a part of (e.g. 127 shifts)
  Cyclic shift given by both the remaining part of and (e.g. 3x3 shifts)

## Slide 6: Appendix B
Option 2:
  M-sequences , , ..., are given by preferred tuple of polynomials
    For example in case of r=3,
      for , for , and for
  M-sequence is given by the another polynomial
  Sequence index given by a part of (e.g. 3 sequences)
  Cyclic shift given by the remaining part of (e.g. 127 shifts)
  Cyclic shift given by (e.g. 3 shifts)