## Slide 1: WF on NR-RACH preamble formats
ZTE
3GPP TSG RAN WG1 Ad Hoc Meeting
HangZhou, China 15th – 19th March 2017
Agenda: 7.1.1.4.1
R1-1709260

## Slide 2: Background
Following remaining issues need to be finalized in the next meeting
  RACH preamble sequence length and subcarrier spacing
    Selection of L between L = 63/71 and L = 127/139
    Further down-selection of subcarrier spacing if needed
  RACH format design
    Supported preamble formats of option 1 and detailed design of each
    Whether/how to support option 2 and option 4
    CP/GT length

## Slide 3: Proposal
  Agree on a set of preamble formats to be supported by option 1, these preamble formats shall cover the most important use cases.
  We should strive to make in the order of less than 10 formats in total for both below and above 6GHz.
    Note: When needed, new formats for optimization could be introduced

## Slide 4: Proposal on premble formats for L = 839
Format | L | SCS(kHz) | BW (MHz) | N_OS | N_RP | T_SEQ (Ts) | T_CP (Ts) | T_GP (Ts) | Use case
0 | 839 | 1.25 | 1.08 | 2 | 1 | 2*24576 | 21024 | 21904 | Large cell, upto 100km
1 | 839 | 1.25 | 1.08 | 1 | 1 | 24576 | 3168 | 2975 | LTE refarming
2 | 839 | 2.5 | 2.16 | 1 | 1 | 12888 | 1548 | 1488 | Up to 7km cell
3 | 839 | 2.5 | 2.16 | 2 | 1 | 2*12888 | 21024 | 15840 | High speed case, 500km/h
4 | 839 | 2.5 | 2.16 | 4 | 1 | 4*12888 | 6240 | 6048 | Coverage enhancement
5 |  |  |  |  |  |  |  |  | 
Note:
L is the sequence lenght
Ts = 1/(30720) ms